Confidential

Government Pensions Administration Agency (GPAA)

Request for Proposals for the Supply and Installation of Energy efficiency light fittings at the GPAA Head Office:

ALL BID DOCUMENTS TO BE DEPOSITED AT THE TENDER BOX SITUATED AT THE RECEPTION AREA AT:

34 HAMILTON STR

ARCADIA

PRETORIA

#### TABLE OF CONTENTS

|  | PAGES |
| --- | --- |
| Notice to Tenderers |  |
| Section 1 – General | 5 – 10 |
| Section 2 – Detailed specification electrical installation | 11 – 13 |
| Section 3 – Quality Specification for material and electrical installation | 14 – 21 |
| Section 4 – Technical specification | 22 - 23 |
| Section 5 – Evaluation Criteria | 24 |
| Section 6 – SBD Forms | 25 - 60 |

SECTION 1 – GENERAL

### TABLE OF CONTENTS

| Clause |  | Page |
| --- | --- | --- |
|  | Intent of Specification……………………………………………………. | 5 |
|  | Drawings…………….……………………………………………………. | 5 |
|  | Regulations……………………………………………………………….. | 5 |
|  | Scope of Work……………………………………………………………. | 5 |
|  | Co-ordination……………………………………………………………… | 5 |
|  | Schedule of fittings……………………………………………………….. | 6 |
|  | Quality of materials...……….……………………………………………. | 6 |
|  | Conduit and accessories…..…………………………………………….. | 6 |
|  | Conduit in roof spaces...…………………………………………………. | 7 |
|  | Surface mounted conduit………………………………………………. | 7 |
|  | Conduit in concrete slabs………………………………………………. | 8 |
|  | Wiring……………………………………………………………………... | 8 |
|  | Switches and Socket outlets……………………………………………. | 9 |
|  | Workmanship and staff …………………………………………………. | 9 |
|  | Certificate of compliance………………………………………………… | 9 |
|  | Earthing and installation…………………………………………………. | 9 |
|  | Mounting and positioning of luminaires………………………………… | 10 |

#### SECTION 1 – GENERAL

- Intent of Specification

The specification is intended to cover the removal of existing light fittings and the complete supply and installation of energy efficient light fittings. The minimum equipment requirements are outlined, but do not cover all the details of design and construction. Such details are recognised as being the exclusive responsibility of the contractor.

- Drawings

The Engineer’s drawings covering the various sections of the installation are as stipulated below form part of this contract. The working drawings applicable to this contract shall generally consist of:

- Block C First Floor

- Block D2

- Block E204

- Block H Basement

- Block D Lower ground

- Regulations

The installation shall be constructed and tested in accordance with the following Acts and regulations:

- The latest issue of SABS 0142: “Code of Practice for the Wiring of Premises”,

- The Occupational Health and Safety Act, 1993 (Act 85 of 1993) ,

- The Local Government Act 1998 (Act 10 of 1998 municipal by-laws and any special requirements of the local supply authority,

- The Fire Brigade services Act 1993 Act 2000 (Act 14 of 2000),

- The National Building Regulations and Building Standards Act 1996 (Act 29 of 1996),

- The Post Office Act 1998 (Act 14 of 1998),

- The Electricity Act 1996 (Act 88 of 1996) and

- The Regulations of the local Gas Board where applicable.

- Scope of Work

The supply and installation of energy efficient light fittings as specified in this document.

This will include the removal of existing light fittings and all alterations as required by the Contractor for the installation of the energy efficient light fittings.

- Co-ordination

The GPAA shall not bear liability for any financial implications resulting from delays due to a lack of co-ordination by the Contractor.

- SCHEDULE OF FITTINGS

In all instances where schedule of light, socket outlet and power points are attached to or included on the drawings, these schedules are to be regarded as forming part of the specification.

- QUALITY OF MATERIALS

Only materials of first class quality shall be used and all materials shall be subject to the approval of the Engineer. Wherever applicable the material is to comply with the relevant South African Bureau of Standards, specifications, or to British Standard Specifications, where no SABS Specifications exist.

Materials wherever possible, must be of South African manufacture.

- CONDUIT AND ACCESSORIES

The type of conduit and accessories required for the service, i.e. whether the  conduit and accessories shall be of the screwed type, plain-end type or of the non-metallic type and whether metallic conduit shall be black enamelled or galvanised, is specified in Part 2  of this specification.

Unless   other methods of installation are specified for certain circuits, the installation shall be in conduit throughout.  No open wiring in roof spaces or elsewhere will be permitted.

The conduit and conduit accessories shall comply fully with the applicable SABS specifications as set out below and the conduit shall bear the mark of approval of the South African Bureau of Standards.

- Screwed metallic conduit and accessories:  SABS 1065, parts 1 and   2.

- Plain-end metallic conduit and accessories:  SABS 1065, parts 1 and 2.

- Non-metallic conduit and accessories:  SABS 950

All conduit fittings except couplings shall be of the inspection type.  Where cast metal conduit accessories are used, these shall be of malleable iron.  Zinc base fittings will not be allowed.

Bushes used for metallic conduit shall be brass and shall be provided in addition to locknuts at all points where the conduit terminates at switchboards, switch-boxes, draw-boxes, etc.

Draw-boxes are to be provided in accordance with the “Wiring Code” and wherever necessary to facilitate easy wiring.

For light and socket outlet circuits, the conduit used shall have an external diameter of 20mm.  In all other instances the sizes of conduit shall be in accordance with the “Wiring Code”  for the specified number and size of conductors, unless otherwise directed in part 2 of this specification or indicated on the drawings.

Only one manufactured type of conduit and conduit accessories will be permitted throughout the installation.

Running joints in screwed conduit are to be avoided as far as possible and all conduit systems shall be set or bent to the required angles.  The use of normal bends must be kept to a minimum with exception of larger diameter conduits where the use of such bends is essential.

All metallic conduit shall be manufactured of mild steel with a minimum thickness of 1,2mm for plain-end conduit and 1,6mm in respect of screwed conduit.

Under no circumstances will conduit having a wall thickness of less than 1,6mm be allowed in screeding laid on top of concrete slabs.

Bending and setting of conduit must be done with special bending apparatus manufactured for the purpose and which are obtainable from the manufacturers of the conduit systems.

Damage to conduit resulting from the use of incorrect bending apparatus or methods applied must on indication by the Engineer’s inspectorate staff, be completely removed and rectified and any wiring already drawn into such damaged conduits must be completely renewed at the Contractor’s expense.

Conduit and conduit accessories used for flame-proof or explosion proof installations and for the suspension of luminaires as well as all load bearing conduit shall in all instances be of the metallic screwed type.

All conduit and accessories used in areas within 50 km of the coast shall be galvanised to SABS 763.

Tenderers must ensure that general approval of the proposed conduit system to be used is obtained from the local electricity supply authority prior to the submission of their tender.  Under no circumstances will consideration be given by the Engineer to any claim submitted by the Contractor which may result from a lack of knowledge in regard to the supply authority’s requirements.

- CONDUIT IN ROOF SPACES

Conduit in roof spaces shall be installed parallel or at right angles to the roof members and shall be secured at intervals not exceeding 1,5m by means of saddles screwed to the roof timbers.

Nails will not be allowed.

Where non-metallic conduit has been specified for a particular service, the conduit shall be supported and fixed with saddles with a maximum spacing of 450 mm.  The Contractor shall supply and install all additional supporting timbers in the roof space as required.

Under flat roofs, in false ceilings or where there is less than 0,9m of clearance, or should the ceilings be insulated with glass wool or other insulating material, the conduit shall be installed in such a manner as to allow for all wiring to be executed from below the ceilings.

Conduit runs from distribution boards shall, where possible terminate in fabricated sheet steel draw-boxes installed directly above or in close proximity to the boards.

- SURFACE MOUNTED CONDUIT

Wherever possible, the conduit installation is to be concealed in the building work; however, where unavoidable or otherwise specified under Part 2 of the specification, conduit installed on the surface must be plumbed or levelled and only straight lengths shall be used.

The use of inspection bends is to be avoided and instead the conduit shall be set uniformly and inspection coupling used where necessary.

No threads will be permitted to show when the conduit installation is complete, except where running couplings have been employed.

Running couplings are only to be used where unavoidable, and shall be fitted with sliced couplings as a lock-nut.

Conduit is to be run on approved spaced saddles rigidly secured to the walls.

Alternatively, fittings, tees, boxes, couplings etc., are to be cut into the surface to allow the conduit to fit flush against the surface.  Conduit is to be bedded into any wall irregularities to avoid gaps between the surface and the conduit.

Crossing of conduits is to be avoided; however, should it be necessary purpose-made metal boxes are to be provided at the junction.  The finish of the boxes and positioning shall be in keeping with the general layout.

Where several conduits are installed side by side, they shall be evenly spaced and grouped under one purpose-made saddle.

Distribution boards, draw-boxes, industrial switches and socket outlets etc., shall be neatly recessed into the surface to avoid double sets.

In situations where there are no ceilings the conduits are to be run along the wall plates and the beams.

Painting of surface conduit shall match the colour of the adjacent wall finishes.

Only approved plugging materials such as aluminium inserts, fibre plugs, plastic plugs, etc., and round-head screws shall be used for fixing saddles, switches, socket outlets, etc., to walls, wood plugs and the plugging in joints in brick walls are not acceptable.

- CONDUIT IN CONCRETE SLABS

In order not to delay building operations the Contractor must ensure that all conduits and other electrical equipment, which are to be cast in the concrete columns and slabs, are installed in good time.

The Contractor shall have a representative in attendance at all times when the casting of concrete takes place.

Draw-boxes, expansion joint boxes and round conduit boxes are to be provided where necessary.  Sharp bends of any nature will not be allowed in concrete slabs.

Draw and/or inspection boxes shall be grouped under one common cover plate and must preferable installed in passages or male toilets.

All boxes, etc., are to be securely fixed to the shuttering to prevent displacement when concrete is cast.  The conduit shall be supported and secured at regular intervals and installed as close as possible to the neutral axis of concrete slabs and/or beams.

Before any concrete slabs are cast, all conduit droppers to switchboards shall be neatly spaced and rigidly fixed.

- WIRING:

Except where otherwise specified in Part 2 of this specification, wiring shall be carried out in conduit throughout.  Only one circuit per conduit will be permitted.

No wiring shall be drawn into conduit until the conduit installation has been completed and all conduit ends provided with bushes.  All conduit to be clear of moisture and debris before wiring is commenced. Unless otherwise specified in Part 2 of this specification or indicated on the service drawings, the wiring of the installation shall be carried out in accordance with the “Wiring Code”.  Further to the requirements concerning the installation of earth conductors to certain light points as set out in the “Wiring Code”, it is a specific requirement of this document that where plain-end

Metallic conduit or non-metallic conduit has been used, earth conductors must be provided and drawn into the conduit with the main conductors to all points, including all luminaires and switches throughout the installation.

Wiring for lighting circuits is to be carried out with 2,5mm² conductors and a 2,5mm² earth conductor.  For socket outlet circuits the wiring shall comprise 4mm² conductors and a 2,5mm² earth conductor.  In certain instances, as will be directed in Part 2 of this specification, the sizes of the aforementioned conductors may be increased for specified circuits.  Sizes of conductors to be drawn into conduit in all other instances, such as feeders to distribution boards, power points etc., shall be as specified elsewhere in this specification or indicated on the drawings.  Sizes of conductors not specified must be determined in accordance with the “Wiring Code”.

The loop-in system shall be followed throughout, and no joints of any description will be permitted.

The wiring shall be done in PVC insulated 600/1000 V grade cable to SABS 150.

Where cable ends connect onto switches, luminaires etc., the end strands must be neatly and tightly twisted together and firmly secured.  Cutting away of wire strands of any cable will not be allowed.

- SWITCHES AND SOCKET OUTLETS

All switches and switch-socket outlet combination units shall conform to the Engineer Quality Specifications which form part of this specification.

No other than 16A 3 pin sockets are to be used, unless other special purpose types are distinctly specified or shown on the drawings.

All light switches shall be installed at 1,4m above finished floor level and all socket outlets as directed in the Schedule of Fittings which forms part of this specification or alternatively the height of socket outlets may be indicated on the drawings.

- WORKMANSHIP AND STAFF

Except in the case of electrical installations supplied by a single phase electricity supply at the point of supply, an accredited person shall exercise general control over all electrical installation work being carried out.

The workmanship shall be of the highest grade and to the satisfaction of the Engineer.

All inferior work shall, on indication by the Engineer’s inspecting officers, immediately be removed and rectified by and at the expense of the Contractor.

- CERTIFICATE OF COMPLIANCE

On completion of the service, a certificate of compliance must be issued to the Engineer’s Representative/Agent in terms of the Occupational Health and Safety Act,  1993  (Act 85 of 1993).

- EARTHING OF INSTALLATION

Ring Mains

Common earth conductors may be used where various circuits are installed in the same wire way in accordance with SABS 0142.  In such instances the sizes of earth conductors shall be equivalent to that of the largest current carrying conductor installed in the wire way, alternatively the size of the conductor shall be as directed by the Engineer.  Earth conductors for individual circuits branching from the ring main shall by connected to the common earth conductor with T-ferrules or soldered.  The common earth shall not be broken.

Non-metallic Conduit

Where non-metallic conduit is specified or allowed, the installation shall comply with the Engineer’s standard quality specification for “conduit and conduit accessories”.

Standard copper earth conductors shall be installed in the conduits and fixed securely to all metal appliances and equipment, including metal switch boxes, socket-outlet boxes, draw-boxes, switchboards, luminaires, etc. The securing of earth conductors by means of self-threading screws will not be permitted.

Flexible Conduit

An earth conductor shall be installed in all non-metal flexible conduit.  This earth conductor shall not be installed externally to the flexible conduit but within the conduit with the other conductors.  The earth conductor shall be connected to the earth terminals at both ends of the circuit.

Connection

Under no circumstances shall any connection points, bolts, screws, etc., used for earthing be utilised for any other purpose.  It will be the responsibility of the Contractor to supply and fit earth terminals or clamps on equipment and materials that must be earthed where these are not provided.

Unless earth conductors are connected to proper terminals, the end shall be tinned and lugged.

- MOUNTING AND POSITIONING OF LUMINAIRES

The Contractor is to note that in the case of board and acoustic tile ceilings, i.e. as opposed to concrete slabs, close co-operation with the building contractor is necessary to ensure that as far as possible the luminaires are symmetrically positioned with regard to the ceiling pattern.

The lay-out of the luminaires as indicated on the drawings must be adhered to as far as possible and must be confirmed with the Engineer’s representative.

Fluorescent luminaires installed against concrete ceilings shall be screwed to the outlet boxes and in addition 2 x 6mm expansion or other approved type fixing bolts are to be provided.  The bolts are to be ¾ of the length of the luminaires apart.

Fluorescent luminaires to be mounted on board ceilings shall be secured by means of two 40mm x No. 10 round head screws and washers.  The luminaires shall also be bonded to the circuit conduit by means of locknuts and brass bushes.  The fixing screws are to be placed ¾ of the length of the fitting apart.

Earth conductors must be drawn in with the circuit wiring and connected to the earthing terminal of all fluorescent luminaires as well as other luminaires exposed to the weather in accordance with the “Wiring Code”.

Incandescent luminaires are to be screwed directly to outlet boxes in concrete slabs.  Against board ceilings the luminaires shall be secured to the brandering or joists by means of two 40mm x No. 8 round head screws.

SECTION 2

DETAILED SPECIFICATION

ELECTRICAL INSTALLATION

DETAIL SPECIFICATION

- ELECTRICAL EQUIPMENT

All equipment and fittings supplied must be in accordance with the attached quality specification (Section 3 of this document), suitable for the relevant supply voltage, and frequency and must be approved by the Engineer’s representative.

- DRAWINGS

The drawings generally show the scope and extent of the proposed work and shall not be held as showing every minute detail of the work to be executed.

The position of power points, switches and light points that may be influenced by built-in furniture must be established on site, prior to these items being built in.

- BALANCING OF LOAD

The Contractor is required to balance the load as equally as possible over the multiphase supply.

- SERVICE CONDITIONS

All plant shall be designed for the climatic conditions appertaining to the service.

- SWITCHES AND SOCKET   OUTLETS

The installation of switches and socket outlets must conform to clause 13 of Part 1 of this specification.

- LIGHT FITTINGS AND LAMPS

The installation and mounting of luminaires must conform with clause 19 of Part 1 of this specification.

All fittings to be supplied by the Contractor shall have the approval of the Engineer.  Incandescent lamps shall bear the approved mark of the S.A.B.S. and shall have the British light centre length.

The light fittings must be of the type specified in the Schedule of Light Fittings

- MAINTENANCE OF ELECTRICAL SUPPLY

All interruptions of the electrical supply that may be necessary for the execution of the work, will be subject to prior arrangement between the Contractor and the user Engineer and the Engineer’s representative.

- EXTENT OF WORK

The work covered by this contract comprises the complete electrical installation, in working order, as shown on the drawings and as per this specification, including the supply and installation of all fittings and also the installation of such equipment supplied by the Engineer.

- CONDUIT AND WIRING

Conduit and conduit accessories shall be black enamelled/galvanized screwed conduit or black enamelled/galvanized plain end conduit in accordance with SABS 162, 763 and 1007 respectively.

All conduit, regardless of the system employed, shall be installed strictly as described in the applicable paragraphs of clauses 4 to 8 of Part 1 of the specification.  Wiring of the installation shall be carried out as directed in clause 9 part 1 of this specification.

Where plain end conduit is offered all switches and light fittings must be supplied with a permanent earth terminal for the connection of the earth wire.

Lugs held by switch fixing screws or self-tapping screws will not be acceptable.

- POWER TRUNKING

The Contractor shall be responsible for the supply and installation of all power trunking complete with corner pieces, end pieces, junction pieces, supply conduits, cover plates and power outlets as specified and indicated on the drawings.

The power trunking must comply with SABS 1197.  The Contractor must ensure that the power trunking is installed to satisfaction of the Engineer’s representative before commencing with the wiring of the power trunking.

- SCHEDULE OF LIGHT FITINGS

The light fittings and accessories are to be according to the quality specifications in Part 3 and shall be approved by the Engineer / Engineer representative.

Type 4A:	1500mm Open Channel Fluorescent luminaire LLB suitable for ceiling mounting, complete with 2 x 58W tube switch start with SABS mark.

Type T5:	1200mm Open Channel Fluorescent luminaire LLB suitable for ceiling mounting, complete with 2 x 36W tube switch start with SABS mark.

Type L3:	1200mm x 600mm Recessed Mounted Fluorescent luminaire LLB complete with 3 x 36W tube switch start with SABS mark.

Type B:	Round Bulkhead Fluorescent luminaire complete with 2 x 18W tube switch start with SABS mark

SECTION 3

QUALITY SPECIFICATION FOR MATERIAL

AND

ELECTRICAL INSTALLATIONS

SPECIFICATION FOR ELECTRICAL INSTALLATIONS

SECTION 3

QUALITY SPECIFICATION FOR MATERIAL AND EQUIPMENT OF ELECTRICAL INSTALLATIONS:

- CONDUIT AND ACCESSORIES.

The type of conduit and accessories required for the service, i.e. whether the conduit and accessories shall be of the screwed type, plain-end type or of the non-metallic type and whether metallic conduit shall be black enamelled or galvanised, is specified in Section 2 of this specification. Unless other methods of installation are specified for certain circuits, the installation shall be in conduit throughout. No open wiring in roof spaces or elsewhere will be permitted.

The conduit and conduit accessories shall comply fully with the applicable SABS specifications as set out below and the conduit shall bear the mark of approval of the South African Bureau of Standards.

(a) 	Screwed metallic conduit and accessories: SABS 1065 section 1 and 2.

(b) 	Plain-end metallic conduit and accessories: SABS 1065 section 1 and 2.

(c)	Non-metallic conduit and accessories: SABS 950

All conduit fittings except couplings shall be of the inspection type. Where cast metal conduit accessories are used, these shall be of malleable iron. Zinc base fittings will not be allowed.

Bushes used for metallic conduit shall be brass and shall be provided in addition to lock nuts at all points where the conduit terminates at switchboards, switch-boxes, draw-boxes, etc.

Draw-boxes are to be provided in accordance with the "Wiring Code" and wherever necessary to facilitate easy wiring.

For light and socket outlet circuits, the conduit used shall have an external diameter of 20mm.  In all other instances the sizes of conduit shall be in accordance with the "Wiring Code" for the specified number and size of conductors, unless otherwise directed in section 2 of this specification or indicated on the drawings.

Only one manufacture of conduit and conduit accessories will be permitted throughout the installation.

Running joints in screwed conduit are to be avoided as far as possible and all conduit systems shall be set or bent to the required angles.  The use of normal bends must be kept to a minimum with exception of larger diameter conduits where the use of such bends is essential.

All metallic conduits shall be manufactured of mild steel with a minimum thickness of 1,2mm for plain-end conduit and 1.6mm in respect of screwed conduit.

NOTE

Under no circumstances will conduit having a wall thickness of less than 1,6mm be allowed in screeding laid on top of concrete slabs.

Bending and setting of conduit must be done with special bending apparatus manufactured for the purpose and which are obtainable from the manufacturers of the conduit systems.  Damage to conduit resulting from the use of incorrect bending apparatus or methods applied must on indication by the Engineer's inspectorate staff, be completely removed and rectified and any wiring already drawn into such damaged conduits must be completely renewed at the contractor's expense.

Conduit and conduit accessories used for flame-proof or explosion proof installations and for the suspension of luminaires as well as all load bearing conduit shall in all instances be of the metallic screwed type.

All conduit and accessories used in areas within 50km of the coast shall be galvanised to SABS 763.

Tenderers must ensure that general approval of the proposed conduit system to be used is obtained from the local electricity supply authority prior to the submission of their tender.  Under no circumstances will consideration be given by the Engineer to any claim submitted by the contractor which may result from a lack of knowledge in regard to the supply authority's requirements.

- CONDUIT IN ROOF SPACES.

Conduit in roof spaces shall be installed parallel or at right angles to the roof members and shall be secured at intervals not exceeding 1,5m by means of saddles screwed to the roof timbers.

Nails will not be allowed.

Where non-metallic conduit has been specified for a particular service, the conduit shall be supported and fixed with saddles with a maximum spacing of 450mm throughout the installation.  The contractor shall supply and install all additional supporting timbers in the roof space as required.

Under flat roofs, in false ceilings or where there is less than 0,9m of clearance, or should the ceilings be insulated with glass wool or other insulating material, the conduit shall be installed in such a manner as to allow for all wiring to be executed from below the ceilings.

Conduit runs from distribution boards shall, where possible terminate in fabricated sheet steel draw-boxes installed directly above or in close proximity to the boards.

SURFACE MOUNTED CONDUIT.

Wherever possible, the conduit installation is to be concealed in the building work; however, where unavoidable or otherwise specified under Section 2 of the specification, conduit installed on the surface must be plumbed or levelled and only straight lengths shall be used.

The use of inspection bends is to be avoided and instead the conduit shall be set uniformly and inspection coupling used where necessary.

No threads will be permitted to show when the conduit installation is complete, except where running couplings have been employed.

Running couplings are only to be used where unavoidable, and shall be fitted with a sliced coupling as a locknut.

Conduit is to be run on approved spaced saddles rigidly secured to the walls.

Alternatively, fittings, tees, boxes, couplings etc., are to be cut into the surface to allow the conduit to fit flush against the surface. Conduit is to be bedded into any wall irregularities to avoid gaps between the surface and the conduit.

Crossing of conduits is to be avoided, however, should it be necessary purpose-made metal boxes are to be provided at the junction.  The finish of the boxes and positioning shall be keeping with the general layout.

Where several conduits are installed side by side, they shall be evenly spaced and grouped under one purpose-made saddle.

Distribution boards, draw-boxes, industrial switches and socket outlets etc., shall be neatly recessed into the surface to avoid double sets.

In situations where there are no ceilings the conduits are to be run along the wall plates and tie beams.

In buildings where building operations are to be carried out, all surface conduit will be painted by the building contractor.

In all other instances the electrical contractor shall allow for painting of surface conduit with two coats of good quality enamel paint, and the colour shall match the surrounding building finish.

Only approved plugging materials such as aluminium inserts, fibre plugs, plastic plugs, etc., and around head screws shall be used for fixing saddles, switches, socket outlets, etc., to walls, wood plugs and the plugging in joints in brick walls are not acceptable.

- TUBULAR FLUORESCENT LAMP LUMINAIRES FOR INTERIOR APPLICATIONS

3.1.	GENERAL

3.1.1	To promote work creation in South Africa, the luminaire should preferably be manufactured within the Republic of South Africa and should have a local content of at least 50%.

3.1.2	If the luminaire offered is of foreign origin, full specifications on technical performance and quality must be submitted and full reasons shall be given why the unit had to be imported.

3.1.3	A sample luminaire shall be provided for evaluation and approval by the Electrical Engineer prior to installation.

3.1.4	Luminaires, associated equipment and control gear shall be new and unused and shall be supplied complete with lamps, control gear, diffusers, mounting brackets, etc. and shall be delivered to site in a protective covering.

3.1.5	Lamps shall be delivered separately.

3.2.	STANDARDS

The following standard specifications of the South-African Bureau of Standards shall apply to this luminaire specification:

3.2.1	SABS 1119: 		Interior luminaires for fluorescent lamps.

3.2.2	SABS 1250: 		Capacitors for use with fluorescent and other discharge lamp ballasts.

3.2.3	SABS 890: 		Ballast’s for fluorescent lamps.

3.2.4	SABS 1464: 		Safety of luminaires.

3.2.5	SABS 1479: 		Glow starters for fluorescent lamps.

3.2.6	SABS IEC 400: 		Lamp holders for tubular fluorescent lamps.

3.2.7	SABS 1041: 		Tubular fluorescent lamps for general service.

3.2.8	SABS 1247: 		Coatings applied by the powder-coating process.

3.2.9	SABS 783: 		Baked enamels.

3.2.10	SABS 0142: 		The wiring of Premises

3.2.11	Any standard referred to in the above specifications.

4.	PHYSICAL AND ENVIRONMENTAL REQUIREMENTS

4. 1	AREAS OF APPLICATION: The luminaires are intended for standard indoor use in buildings under the control of the Engineer of Public Works.

4. 2	FIXING: The luminaires shall be suitable for mounting in or against ceilings as described in the project specification.

4. 3	ENVIRONMENTAL: Unless otherwise specified in the detail specification the luminaires shall be suitable for operation in ambient temperatures between -10°C and +25°C.

4. 4	SAFETY: The luminaire shall bear the SABS 1464 safety mark.

    - NOISE: Noisy ballasts will not be accepted and shall be replaced at no cost to the Engineer. All ballasts shall comply with the requirements of the latest edition of SABS 890, Part 1.

5.	GENERAL TECHNICAL REQUIREMENTS

5.1	GENERAL

5.1.1	Tubular fluorescent lamp luminaires shall comply fully with SABS 1119 and all amendments as well as the additional requirements of this specification. Luminaires shall bear the SABS mark, or at least have a SABS Certificate of Compliance.

5.1.2	The Engineer reserves the right to have samples of luminaires offered tested by the SABS for compliance with SABS 1119.  If a sample luminaire is found not to comply with SABS 1119 the cost of such tests shall be borne by the Tenderer.

5.2	CONSTRUCTION add spec

5.2.1	A luminaire shall consist of a ventilated body manufactured of cold rolled sheet steel not less than 0,8mm thick, suitably braced or stiffened to prevent distortion.  The body shall be of sufficient strength for the mounting of the entire luminaire.

    - The luminaire shall be designed to accommodate the control gear, wiring, lamp holders and, where

applicable, the diffuser and reflectors.  It shall be possible to reach the control gear without disconnecting wiring or removing the luminaire.

5.2.3	Except for mounting holes and/or slots and the required openings in air-return luminaires, the back of the body channel shall be closed over the full length of the luminaire.

5.2.4	Suitable knockouts shall be provided in the rear of the luminaire body for wire entry.

5.2.5	All components, including screws, bolts and nuts utilised in the construction of the luminaire or

Fixing of its components, shall be corrosion proof. Cadmium plated or stainless steel materials are preferred.

5.3	INTERNAL WIRING

5.3.1	Luminaires shall be completely wired internally. Conductors shall be protected with grommets where they pass through holes in the body.

5.3.2	The wiring shall be totally metal enclosed to prevent any possible contact with live components while changing lamps.

5.3.3	The conductor insulation shall be rated to withstand the temperature inside the luminaire body without deterioration.

5.3.4	The wiring shall terminate on a suitable terminal block having screw down plates bearing on the wires.  Terminals where screws bear down directly on wires will not be acceptable.

5.3.5	An earth terminal, welded to the luminaire body, shall be provided.  To ensure good earth continuity the earth terminal shall not be spray painted.  The earth conductor shall be connected to this terminal by means of a crimped lug.

5.4	LAMP HOLDERS

Lamp holders shall preferably be of the telescopic spring-loaded type.  Where twist-lock type lamp holders are provided, the mounting of the holders shall be able to accommodate the tolerances experienced in the length of lamps and in the manufacture of luminaires.

5.5	CONTROL GEAR

5.5.1	The control gear, ballasts, capacitors and starters shall be designed and manufactured to suit the control circuitry adopted.  All luminaires shall operate on a switch-start basis.

5.5.2	Ballasts shall comply with SABS 890 and SABS 891, suitable for operation on 220V to 250V, 50Hz supplies.

5.5.3	Ballasts shall further be suitable for the particular luminaire to ensure that the thermal limits specified in paragraph 3.5 of SABS 1119 are not exceeded.

5.5.4	Starters shall comply with SABS 1479 or with BS 3772 if it is not covered by SABS 1479.  Starters with metal cans shall contain integral earthing facilities to earth the can upon insertion.

5.5.5	Starters shall be accessible from the outside of the luminaire, and the replacement of the starter shall not necessitate the removal of lamps.

5.6	CAPACITORS

Capacitors shall comply with SABS 1250.  The power factor of each complete fitting shall be corrected to at least 0, 85.

5.7	LAMPS

5.7.1	Fluorescent lamps shall be suitable for the control circuitry used.  Lamps shall comply with SABS 1041.

5.7.2	If no colour is specified in the Detail Technical Specification, the light colour shall correspond to colour 2 (4 300K) of SABS 1041.

5.7.3	Lamps of the same colour shall be provided for an entire installation unless specified to the contrary.

5.7.4	There shall be no visible flicker in the lamps and lamps shall readily strike when switched on.  Faulty lamps or ballasts shall be replaced at no cost to the Engineer.

6.7.	TECHNICAL INFORMATION

The Tenderer shall include full technical particulars regarding the luminaire offered with the tender.

6.8.	CHANNEL LUMINAIRE

6.8.1	Channel luminaires shall consist of a ventilated, enclosed channel body with one or more lamps as specified in the project specification.  The channel body shall house the ballast, capacitor, terminals and internal wiring.

6.8.2	Provision shall be made for the addition of reflector wings and/or diffusers.

6.8.3	Three sets of mounting slots and knock-outs suitable for mounting onto standard round conduit boxes and/or 20mm diameter conduit pendant rods, shall be provided in the rear of the channel, one in the centre and one approximately one sixth from each end.

6.8.4	A knockout suitable for a 20mm diameter conduit entry shall be provided at each end of the channel.  The distance between the back of the luminaire and centre of the knockout shall be approximately 25mm.

6.8.5	The knockouts shall be positioned on the centre line of the channel.

6.8.6	The body channel shall incorporate a removable cover acting as a reflector, manufactured of cold rolled steel, not less than 0,8mm thick, designed and mounted to completely cover the interior of the body channel and its contents and extending over the full length of the luminaire up to the lamp holders.

6.8.7	The reflector shall be firmly held in position with a latching device consisting of knurled, coin slot, captive screws.  Plastic, used as a spring mechanism, is not acceptable as a fixing device for reflectors.  The action of the latching device shall not deteriorate due to use and/or ageing.

6.9 	RECESSED LUMINAIRES

6.9.1    Recessed luminaires shall be suitable for mounting in the ceiling structure specified in the project specification.

6.9.2	The attachment of the prismatic diffuser or reflector shall be similar to that specified in paragraph 10 above.

6.9.3	The diffuser or reflector shall fit flush with the ceiling and the only visible portion shall be the reflector or diffuser.

6.9.4	Should the luminaire be so designed that a surrounding frame is visible, then this frame shall be manufactured of anodised aluminium.  The frame shall form a neat trim with the ceiling.  The corners of the surrounding frame shall be mitred and reinforced.

6.10.	LOW-BRIGHTNESS LUMINAIRES

6.10.1	The luminaire shall be provided with an aluminium louver with V-shaped longitudinal vanes and extruded stepped cross-shielding plates.

6.10.2	Louvers shall be constructed from high purity aluminium (99, 98%), chemically brightened and anodised.

6.10.3	The total Light Output Ratio (LOR) shall be 62% or better. In the plane between 60(and 90(from the vertical, the LOR shall be below 3%.

6.11.	LOW GLARE LUMINAIRES

6.11.1	The luminaire shall be provided with a die-formed, bright anodised high-purity aluminium (99, 98%) louver with parabolic reflecting surfaces in both directions.

6.11.2	The total LOR shall be 62% or better. In the plane between 60 and 90(from the vertical), the LOR shall be less than 1, 3%

6.12.	LUMINAIRES FOR USE IN AREAS WITH VISUAL DISPLAY TERMINALS

6.12.1	The luminaire shall have anodised specular louvers to provide the brightness control required for this type of application.

6.12.2	At angles between 60 and 90(from the vertical) the luminance shall not exceed 200cd/m2.

6.12.3	At the above angles the LOR shall be less than 0, 6%. At angle between the vertical and 60 the LOR shall be 61% or better.

#### SECTION 4 - TECHNICAL SPECIFICATION

General

The GPAA is seeking to appoint a sufficiently experienced service provider to supply and install energy efficiency light fittings at the GPAA head office.

Objective

To minimise the undesirable impacts of energy usage upon the environments and contribute towards secure and affordable energy for the organisation.

Tender Briefing Session

- A compulsory briefing session will be held at the GPAA Head Office, 34 Hamilton Street, Arcadia, Pretoria. Travel and accommodation costs will be on the service provider's account.

Invitation to RFP

- To be considered, each bidder must submit a completed set of the prescribed documents attached to this RFP, accompanied by its proposal, to the GPAA, not later than 11h00 on (07 April 2017).

No other distribution of proposals is to be made by the bidder.  The proposal must include a statement of the period for which the proposal remains valid.  The proposal must be valid for at least one hundred and twenty (120) days from the date of closure.

Incurring of costs:

- The GPAA will not be liable for any cost incurred by any vendor/bidder prior to signing of a binding contract by parties concerned.

Communication during the RFP Process:

- Any communication with respect to this RFP should be directed to the people below:

| Technical Enquiries |
| --- |
| Name: | Rendani Mashawana |
| E-mail: | Rendani.Mashawana@gpaa.gov.za |

Or

| Administrative Enquiries |
| --- |
| Name: | William Ramoroka |
| E-mail: | william.ramoroka@gpaa.gov.za |

- Any communication during the RFP process should be addressed by e-mail.  Telephonic queries will not be entertained.

- All e-mail correspondence must contain the RFP number GPAA 16/2017 in the subject line. All queries will be consolidated and responded to in writing every Friday during the proposal response period, and will be distributed to all the respondents that completed a non-disclosure agreement.  No enquiries will be entertained one week prior to the closing of the RFP.

- Communication with any other personnel of the GPAA, with regard to this RFP is not permitted and will result in disqualification of the relevant RFP response.

Submission Requirements

- Responses to this RFP must be submitted between 07h30 and 16h00 (Monday to Friday, excluding public holidays); on the closing date submissions must be done before 11h00.

- Service providers must submit five (5) hardcopies of the technical response as well as five (5) hardcopies of the financial proposal.

- One hardcopy must be the original submission, clearly marked "Original" and the remaining hardcopies can be a copied versions of the original.

- It is the responsibility of the service provider to record their submission in the register which will be provided at the GPAA Head Office reception desk.

Site Information

13.1	Location

| OFFICE NAME | PROVINCE | LOCATION |
| --- | --- | --- |
| GPAA Head Office | Gauteng (Pretoria) | 34 Hamilton Street |

Completion Time

The Contractor shall ensure that the installation of energy saving lights is complete within 2 months after the awarding of the tender.

| SECTION 5 – EVALUATION CRITERIA |
| --- |
| Item No. | Evaluation Criteria Item 90/10 Principle | Weight |
|  | A |  | Phase 1: Administrative compliance: Fully comply with specification and requirements. • SARS Tax status certificate with PIN number • Completed SBD 3.1;(Pricing proposal) • Completed SBD 4; • Completed SBD 8; • Completed SBD 9; • Technical Response (which includes: company profile, track record and previous experience, capacity and capability Minimum requirement of CIDB Grading 3 EB All SBD forms stated above should be completed in full signed and dated by an authorised representative of the bidder |  |
|  | B |  | PRICE (Phase 2) | 90 |
|  | C |  | B-BBEE Status Level of Contributor | 10 |
|  | Total | 100 |
|  | D |  | Functionality(Phase 3) |  |
|  |  |  | Track Record and Experience –Three (3) years proven experience on similar projects with reference letters from previous and current contactable clients. Capacity – Supported by a minimum of three award letters and completion certificates from previous and current clients. Capability – The service provider must demonstrate that they have necessary capacity to provide the required service, this may include but not limited to the following resources: Relevant Skills and Experience in construction industry which includes construction/civil, electrical and air-conditioning services. Equipment and assets of company Technical Approach - Supported by a detailed project plan Written narrative and/or a method statement. Temporary Access control plan during construction. The plan must include the security plan during the construction as well as how will you comply to OHS requirements | 40 10 10 10 10 10 10 |
|  |  |  | NB Minimum 60% qualifications on functionality |  |
|  |  |  | Sub-total | 100 |
|  |  |  | Total | 100 |

SBD1

INVITATION TO BID

BID NUMBER: GPAA 16/2017                CLOSING DATE: 07 April 2017

CLOSING TIME: 11:00AM

DESCRIPTION:

SPECIFICATION FOR THE SUPPLY AND INSTALLATION OF ENERGY EFFICIENCY LIGHT FITTINGS AT GPAA HEAD OFFICE

BID DOCUMENTS MAY BE POSTED TO OR DEPOSITED IN THE BID BOX SITUATED AT GPAA ADDRESSED TO:

The CEO: Government Pensions Administration Agency

Bid Administration

34 HAMILTON STR

ARCADIA

PRETORIA, TSHWANE

0001

Bidders should ensure that bids are delivered timorously to the correct address. If the bid is late, it will not be accepted for consideration. The bid box is generally open 8 hours a day between 08:00 to 16:30, Monday to Fridays.

ALL BIDS MUST BE SUBMITTED WITH THE STANDARD FORMS – (NOT TO BE RE-TYPED)

THIS BID IS SUBJECT TO THE GENERAL CONDITIONS OF CONTRACT (GCC) AND, IF APPLICABLE, ANY OTHER SPECIAL CONDITIONS OF CONTRACT

NAME OF BIDDER……………………………………………………………………………………………………………

POSTAL ADDRESS………………………………………………………………………………………………………….

STREET ADDRESS…………………………………………………………………………………………………………

TELEPHONE NUMBER CODE……………NUMBER……………………………………………….

CELLPHONE NUMBER ……………………………………….

FACSIMILE NUMBER	CODE ………… NUMBER…………………………………

VAT REGISTRATION NUMBER …………………………………………………………………………

HAS A TAX CLEARANCE CERTIFICATE BEEN SUBMITTED (SBD2)?		YES/NO

SIGNATURE OF BIDDER 	……………………………………………………

DATE	……………………………………………………

CAPACITY UNDER WHICH THIS BID IS SIGNED	……………………………………………

SBD3.1

GPAA HEAD OFFICE - PRICING SCHEDULE – FIRM PRICES

## NOTE:	ONLY FIRM PRICES WILL BE ACCEPTED. NON-FIRM PRICES (INCLUDING PRICES SUBJECT TO RATES OF EXCHANGE VARIATIONS) WILL NOT BE CONSIDERED

## IN CASES WHERE DIFFERENT DELIVERY POINTS INFLUENCE THE PRICING, A SEPARATE PRICING SCHEDULE MUST BE SUBMITTED FOR EACH DELIVERY POINT

Name of bidder…………………………………… Bid number GPAA 16/2017 Closing Time and Date: 11:00AM , 07 April 2017

OFFER TO BE VALID FOR…120…DAYS FROM THE CLOSING DATE OF BID.

| ELECTRICAL INSTALLATION |  |  |  |  |
| --- | --- | --- | --- | --- |
| Internal Installation | BLOCK C-1ST FLOOR |  |
| Item | Description | Unit | Quantity | Rate | Amount |
| 1 | Conduit Work |  |  |  |  |
|  | Supply, delivery and installation of SABS approved PVC Conduits completed with all required conduit accessories. |  |  |  |  |
|  | Built or Chase into brick or concrete work: |  |  |  |  |
| 1.1 | 20mm PVC Conduit | m | 200 |  |  |
| 1.2 | 25mm PVC Conduit | m | 100 |  |  |
|  | Sub Total Carried Forward |  |  |  |  |
| Item | Description | Unit | Quantity | Rate | Amount |
|  | Sub Total Brought Forward |  |  |  |  |
|  | In Ceiling space and Timber work |  |  |  |  |
| 1.3 | 20mm PVC Conduit | m | 100 |  |  |
| 1.4 | 25mm PVC Conduit | m | 50 |  |  |
| 2 | Conduit Boxes |  |  |  |  |
|  | Supply and installation of SABS approved conduit boxes, installed in the run of the conduit installation, cast into concrete and built into brickwork or flush inside false ceiling spaces, complete with all required conduit termination accessories. |  |  |  |  |
| 2.1 | 20mm diameter 4 way type(round box) | No | 30 |  |  |
| 3 | Wall Boxes |  |  |  |  |
|  | Supply and installation of SABS approved galvanised pressed steel wall boxes for building flush into brickwork or cast into concrete work. |  |  |  |  |
|  | Flush mounted type: |  |  |  |  |
| 3.1 | 100 x 50 x 50mm | No | 14 |  |  |
| 4 | PVC Wiring |  |  |  |  |
|  | PVC Wiring in conduits: |  |  |  |  |
| 4.1 | 2.5mm² for lights circuits | m | 1500 |  |  |
| 5 | Stranded Bare Copper Earth Wire |  |  |  |  |
|  | Supply and installation of stranded bare copper earth wire along with PVC wiring in conduits. Tendered rates shall make provision for wastage. |  |  |  |  |
| 5.1 | 1.5mm² | m | 750 |  |  |
|  | Sub Total Carried Forward |  |  |  |  |
| Item | Description | Unit | Quantity | Rate | Amount |
|  | Sub Total Brought Forward |  |  |  |  |
| 6 | Light Fittings |  |  |  |  |
|  | Supply, delivery to site, storage and installation of the below specified light fittings complete with lamps and tubes. Allowance must be made in the rates for all the required fixing materials and accessories. |  |  |  |  |
|  | Fittings to be equal and similar approved to the below quoted manufacture. |  |  |  |  |
| 6.1 | 1200x600 Recessed Fluorescent 3x36W LBR | No | 81 |  |  |
|  | Sub Total Carried Forward |  |  |  |  |
| Item | Description | Unit | Quantity | Rate | Amount |
|  | Sub Total Brought Forward |  |  |  |  |
| 7 | Electrical Tests |  |  |  |  |
|  | Making provision for the required inspection, tests and the commissioning of the complete installation and the issuing of the required certificate. |  |  |  |  |
| 7.1 | Building installation | Sum | 1 |  |  |
| Total for internal installation Carried to Summary of Cost (Excl.VAT) |  |
| Item | Description | Unit | Quantity | Rate | Amount |
|  | Sub Total Brought Forward |  |  |  |  |
| 8 | Demolitions and Alterations |  |  |  |  |
|  | The contractor shall carry out the whole of the works with as little mess and noise as possible and with a minimum of disturbance to adjoining premises and their tenants. He shall provide proper protection and provide, erect and remove when directed, any temporary tarpaulins that may be necessary during the progress of the works, all to the satisfaction of the principal agent. Water supply pipes and other piping that may be encountered and found necessary to disconnect or cut, shall be effectually stopped off or grubbed up and removed, and any new connections that may be necessary shall be made with proper fittings, to the satisfaction of the principal agent |  |  |  |  |
| 8.1 | Removal of the existing light fittings to be stored at GPAA Store room |  |  |  |  |
| 8.2 | Removal of fire detectors, cameras and other items on the ceilings and placing them back after completion |  |  |  |  |
| 8.3 | Make neat to all damages on walls and other items during the alterations |  |  |  |  |
|  | Other (specify) |  |  |  |  |
| Total for Alterations Carried to Summary of Cost (Excl.VAT) |  |

| ELECTRICAL INSTALLATION |  |  |  |  |
| --- | --- | --- | --- | --- |
| Internal Installation | BLOCK D2 |  |  |
| Item | Description | Unit | Quantity | Rate | Amount |
| 1 | Conduit Work |  |  |  |  |
|  | Supply, delivery and installation of SABS approved PVC Conduits completed with all required conduit accessories. |  |  |  |  |
|  | Built or Chase into brick or concrete work: |  |  |  |  |
| 1.1 | 20mm PVC Conduit | m | 200 |  |  |
| 1.2 | 25mm PVC Conduit | m | 100 |  |  |
|  | Sub Total Carried Forward |  |  |  |  |
| Item | Description | Unit | Quantity | Rate | Amount |
|  | Sub Total Brought Forward |  |  |  |  |
|  | In Ceiling space and Timber work: |  |  |  |  |
| 1.3 | 20mm PVC Conduit | m | 100 |  |  |
| 1.4 | 25mm PVC Conduit | m | 50 |  |  |
| 2 | Conduit Boxes |  |  |  |  |
|  | Supply and installation of SABS approved conduit boxes, installed in the run of the conduit installation, cast into concrete and built into brickwork or flush inside false ceiling spaces, complete with all required conduit termination accessories. |  |  |  |  |
| 2.1 | 20mm diameter 4 way type(round box) | No | 30 |  |  |
| 3 | Wall Boxes |  |  |  |  |
|  | Supply and installation of SABS approved galvanised pressed steel wall boxes for building flush into brickwork or cast into concrete work. |  |  |  |  |
|  | Flush mounted type: |  |  |  |  |
| 3.1 | 100 x 50 x 50mm | No | 30 |  |  |
| 4 | PVC Wiring |  |  |  |  |
|  | PVC Wiring in conduits: |  |  |  |  |
| 4.1 | 2.5mm² for lights circuits | m | 2000 |  |  |
| 5 | Stranded Bare Copper Earth Wire |  |  |  |  |
|  | Supply and installation of stranded bare copper earth wire along with PVC wiring in conduits. Tendered rates shall make provision for wastage. |  |  |  |  |
| 5.1 | 1.5mm² | m | 900 |  |  |
|  | Sub Total Carried Forward |  |  |  |  |
| Item | Description | Unit | Quantity | Rate | Amount |
|  | Sub Total Brought Forward |  |  |  |  |
| 6 | Light Fittings |  |  |  |  |
|  | Supply, delivery to site, storage and installation of the below specified light fittings complete with lamps and tubes. Allowance must be made in the rates for all the required fixing materials and accessories. |  |  |  |  |
|  | Fittings to be equal and similar approved to the below quoted manufacture. |  |  |  |  |
| 6.1 | 1200x600 Recessed Fluorescent 3x36W LBR | No | 102 |  |  |
|  | Sub Total Carried Forward |  |  |  |  |
| Item | Description | Unit | Quantity | Rate | Amount |
|  | Sub Total Brought Forward |  |  |  |  |
| 7 | Electrical Tests |  |  |  |  |
|  | Making provision for the required inspection, tests and the commissioning of the complete installation and the issuing of the required certificate. |  |  |  |  |
| 7.1 | Building installation | Sum | 1 |  |  |
| Total for internal installation Carried to Summary of Cost (Excl.VAT) |  |

| Item | Description | Unit | Quantity | Rate | Amount |
| --- | --- | --- | --- | --- | --- |
|  | Sub Total Brought Forward |  |  |  |  |
| 8 | Demolitions and Alterations |  |  |  |  |
|  | The contractor shall carry out the whole of the works with as little mess and noise as possible and with a minimum of disturbance to adjoining premises and their tenants. He shall provide proper protection and provide, erect and remove when directed, any temporary tarpaulins that may be necessary during the progress of the works, all to the satisfaction of the principal agent. Water supply pipes and other piping that may be encountered and found necessary to disconnect or cut, shall be effectually stopped off or grubbed up and removed, and any new connections that may be necessary shall be made with proper fittings, to the satisfaction of the principal agent |  |  |  |  |
| 8.1 | Removal of the existing light fittings to be stored at GPAA Store room |  |  |  |  |
| 8.2 | Removal of fire detectors, cameras and other items on the ceilings and placing them back after completion |  |  |  |  |
| 8.3 | Make neat to all damages on walls and other items during the alterations Other (specify) |  |  |  |  |
| Total for Alterations Carried to Summary of Cost (Excl.VAT) |  |
| ELECTRICAL INSTALLATION |  |  |  |  |
| Internal Installation | BLOCK E204 |  |  |
| Item | Description | Unit | Quantity | Rate | Amount |
| 1 | Conduit Work |  |  |  |  |
|  | Supply, delivery and installation of SABS approved PVC Conduits completed with all required conduit accessories. |  |  |  |  |
|  | Built or Chase into brick or concrete work: |  |  |  |  |
| 1.1 | 20mm PVC Conduit | m | 400 |  |  |
| 1.2 | 25mm PVC Conduit | m | 200 |  |  |
|  | Sub Total Carried Forward |  |  |  |  |
| Item | Description | Unit | Quantity | Rate | Amount |
|  | Sub Total Brought Forward |  |  |  |  |
|  | In Ceiling space and Timber work: |  |  |  |  |
| 1.3 | 20mm PVC Conduit | m | 200 |  |  |
| 1.4 | 25mm PVC Conduit | m | 180 |  |  |
| 2 | Conduit Boxes |  |  |  |  |
|  | Supply and installation of SABS approved conduit boxes, installed in the run of the conduit installation, cast into concrete and built into brickwork or flush inside false ceiling spaces, complete with all required conduit termination accessories. |  |  |  |  |
| 2.1 | 20mm diameter 4 way type(round box) | No | 30 |  |  |
| 3 | Wall Boxes |  |  |  |  |
|  | Supply and installation of SABS approved galvanised pressed steel wall boxes for building flush into brickwork or cast into concrete work. |  |  |  |  |
|  | Flush mounted type: |  |  |  |  |
| 3.1 | 100 x 50 x 50mm | No | 14 |  |  |
| 4 | PVC Wiring |  |  |  |  |
|  | PVC Wiring in conduits: |  |  |  |  |
| 4.1 | 2.5mm² for lights circuits | m | 2500 |  |  |
| 5 | Stranded Bare Copper Earth Wire |  |  |  |  |
|  | Supply and installation of stranded bare copper earth wire along with PVC wiring in conduits. Tendered rates shall make provision for wastage. |  |  |  |  |
| 5.1 | 1.5mm² | m | 1000 |  |  |
|  | Sub Total Carried Forward |  |  |  |  |
| Item | Description | Unit | Quantity | Rate | Amount |
|  | Sub Total Brought Forward |  |  |  |  |
| 6 | Light Fittings |  |  |  |  |
|  | Supply, delivery to site, storage and installation of the below specified light fittings complete with lamps and tubes. Allowance must be made in the rates for all the required fixing materials and accessories. |  |  |  |  |
|  | Fittings to be equal and similar approved to the below quoted manufacture. |  |  |  |  |
| 6.1 | 1200x600 Recessed Fluorescent 3x36W LBR | No | 79 |  |  |
|  | Sub Total Carried Forward |  |  |  |  |
| Item | Description | Unit | Quantity | Rate | Amount |
|  | Sub Total Brought Forward |  |  |  |  |
| 7 | Electrical Tests |  |  |  |  |
|  | Making provision for the required inspection, tests and the commissioning of the complete installation and the issuing of the required certificate. |  |  |  |  |
| 7.1 | Building installation | Sum | 1 |  |  |
| Total for internal installation Carried to Summary of Cost (Excl.VAT) |  |

| Item | Description | Unit | Quantity | Rate | Amount |
| --- | --- | --- | --- | --- | --- |
|  | Sub Total Brought Forward |  |  |  |  |
| 8 | Demolitions and Alterations |  |  |  |  |
|  | The contractor shall carry out the whole of the works with as little mess and noise as possible and with a minimum of disturbance to adjoining premises and their tenants. He shall provide proper protection and provide, erect and remove when directed, any temporary tarpaulins that may be necessary during the progress of the works, all to the satisfaction of the principal agent. Water supply pipes and other piping that may be encountered and found necessary to disconnect or cut, shall be effectually stopped off or grubbed up and removed, and any new connections that may be necessary shall be made with proper fittings, to the satisfaction of the principal agent |  |  |  |  |
| 8.1 | Removal of the existing light fittings to be stored at GPAA Store room |  |  |  |  |
| 8.2 | Removal of fire detectors, cameras and other items on the ceilings and placing them back after completion |  |  |  |  |
| 8.3 | Make neat to all damages on walls and other items during the alterations |  |  |  |  |
|  | Other (specify) |  |  |  |  |
| Total for Alterations Carried to Summary of Cost (Excl.VAT) |  |

| ELECTRICAL INSTALLATION |  |  |  |  |
| --- | --- | --- | --- | --- |
| Internal Installation | BLOCK H-BASEMENT |  |
| Item | Description | Unit | Quantity | Rate | Amount |
| 1 | Conduit Work |  |  |  |  |
|  | Supply, delivery and installation of SABS approved PVC Conduits completed with all required conduit accessories. |  |  |  |  |
|  | Built or Chase into brick or concrete work: |  |  |  |  |
| 1.1 | 20mm PVC Conduit | m | 180 |  |  |
| 1.2 | 25mm PVC Conduit | m | 70 |  |  |
|  | Sub Total Carried Forward |  |  |  |  |
| Item | Description | Unit | Quantity | Rate | Amount |
|  | Sub Total Brought Forward |  |  |  |  |
|  | In Ceiling space and Timber work: |  |  |  |  |
| 1.3 | 20mm PVC Conduit | m | 70 |  |  |
| 1.4 | 25mm PVC Conduit | m | 45 |  |  |
| 2 | Conduit Boxes |  |  |  |  |
|  | Supply and installation of SABS approved conduit boxes, installed in the run of the conduit installation, cast into concrete and built into brickwork or flush inside false ceiling spaces, complete with all required conduit termination accessories. |  |  |  |  |
| 2.1 | 20mm diameter 4 way type(round box) | No | 35 |  |  |
| 3 | Wall Boxes |  |  |  |  |
|  | Supply and installation of SABS approved galvanised pressed steel wall boxes for building flush into brickwork or cast into concrete work. |  |  |  |  |
|  | Flush mounted type: |  |  |  |  |
| 3.1 | 100 x 50 x 50mm | No | 19 |  |  |
| 4 | PVC Wiring |  |  |  |  |
|  | PVC Wiring in conduits: |  |  |  |  |
| 4.1 | 2.5mm² for lights circuits | m | 1700 |  |  |
| 5 | Stranded Bare Copper Earth Wire |  |  |  |  |
|  | Supply and installation of stranded bare copper earth wire along with PVC wiring in conduits. Tendered rates shall make provision for wastage. |  |  |  |  |
| 5.1 | 1.5mm² | m | 850 |  |  |
|  | Sub Total Carried Forward |  |  |  |  |
| Item | Description | Unit | Quantity | Rate | Amount |
|  | Sub Total Brought Forward |  |  |  |  |
| 6 | Light Fittings |  |  |  |  |
|  | Supply, delivery to site, storage and installation of the below specified light fittings complete with lamps and tubes. Allowance must be made in the rates for all the required fixing materials and accessories. |  |  |  |  |
|  | Fittings to be equal and similar approved to the below quoted manufacture. |  |  |  |  |
| 6.1 | 1200x600 Recessed Fluorescent 3x36W LBR | No | 88 |  |  |
|  | Sub Total Carried Forward |  |  |  |  |
| Item | Description | Unit | Quantity | Rate | Amount |
|  | Sub Total Brought Forward |  |  |  |  |
| 7 | Electrical Tests |  |  |  |  |
|  | Making provision for the required inspection, tests and the commissioning of the complete installation and the issuing of the required certificate. |  |  |  |  |
| 7.1 | Building installation | Sum | 1 |  |  |
| Total for internal installation Carried to Summary of Cost (Excl.VAT) |  |

| Item | Description | Unit | Quantity | Rate | Amount |
| --- | --- | --- | --- | --- | --- |
|  | Sub Total Brought Forward |  |  |  |  |
| 8 | Demolitions and Alterations |  |  |  |  |
|  | The contractor shall carry out the whole of the works with as little mess and noise as possible and with a minimum of disturbance to adjoining premises and their tenants. He shall provide proper protection and provide, erect and remove when directed, any temporary tarpaulins that may be necessary during the progress of the works, all to the satisfaction of the principal agent. Water supply pipes and other piping that may be encountered and found necessary to disconnect or cut, shall be effectually stopped off or grubbed up and removed, and any new connections that may be necessary shall be made with proper fittings, to the satisfaction of the principal agent |  |  |  |  |
| 8.1 | Removal of the existing light fittings to be stored at GPAA Store room |  |  |  |  |
| 8.2 | Removal of fire detectors, cameras and other items on the ceilings and placing them back after completion |  |  |  |  |
| 8.3 | Make neat to all damages on walls and other items during the alterations Other (specify) |  |  |  |  |
| Total for Alterations Carried to Summary of Cost (Excl.VAT) |  |

| ELECTRICAL INSTALLATION |  |  |  |  |
| --- | --- | --- | --- | --- |
| Internal Installation | BLOCK D- LOWER GROUND |  |
| Item | Description | Unit | Quantity | Rate | Amount |
| 1 | Conduit Work |  |  |  |  |
|  | Supply, delivery and installation of SABS approved PVC Conduits completed with all required conduit accessories. |  |  |  |  |
|  | Built or Chase into brick or concrete work: |  |  |  |  |
| 1.1 | 20mm PVC Conduit | m | 200 |  |  |
| 1.2 | 25mm PVC Conduit | m | 100 |  |  |
|  | Sub Total Carried Forward |  |  |  |  |
| Item | Description | Unit | Quantity | Rate | Amount |
|  | Sub Total Brought Forward |  |  |  |  |
|  | In Ceiling space and Timber work |  |  |  |  |
| 1.3 | 20mm PVC Conduit | m | 100 |  |  |
| 1.4 | 25mm PVC Conduit | m | 50 |  |  |
| 2 | Conduit Boxes |  |  |  |  |
|  | Supply and installation of SABS approved conduit boxes, installed in the run of the conduit installation, cast into concrete and built into brickwork or flush inside false ceiling spaces, complete with all required conduit termination accessories. |  |  |  |  |
| 2.1 | 20mm diameter 4 way type(round box) | No | 30 |  |  |
| 3 | Wall Boxes |  |  |  |  |
|  | Supply and installation of SABS approved galvanised pressed steel wall boxes for building flush into brickwork or cast into concrete work. |  |  |  |  |
|  | Flush mounted type: |  |  |  |  |
| 3.1 | 100 x 50 x 50mm | No | 20 |  |  |
| 4 | PVC Wiring |  |  |  |  |
|  | PVC Wiring in conduits: |  |  |  |  |
| 4.1 | 2.5mm² for lights circuits | m | 1500 |  |  |
| 5 | Stranded Bare Copper Earth Wire |  |  |  |  |
|  | Supply and installation of stranded bare copper earth wire along with PVC wiring in conduits. Tendered rates shall make provision for wastage. |  |  |  |  |
| 5.1 | 1.5mm² | m | 750 |  |  |
|  | Sub Total Carried Forward |  |  |  |  |
| Item | Description | Unit | Quantity | Rate | Amount |
|  | Sub Total Brought Forward |  |  |  |  |
| 6 | Light Fittings |  |  |  |  |
|  | Supply, delivery to site, storage and installation of the below specified light fittings complete with lamps and tubes. Allowance must be made in the rates for all the required fixing materials and accessories. |  |  |  |  |
|  | Fittings to be equal and similar approved to the below quoted manufacture. |  |  |  |  |
| 6.1 | 1200x600 Recessed Fluorescent 3x36W LBR | No | 111 |  |  |
|  | Sub Total Carried Forward |  |  |  |  |
| Item | Description | Unit | Quantity | Rate | Amount |
|  | Sub Total Brought Forward |  |  |  |  |
| 7 | Electrical Tests |  |  |  |  |
|  | Making provision for the required inspection, tests and the commissioning of the complete installation and the issuing of the required certificate. |  |  |  |  |
| 7.1 | Building installation | Sum | 1 |  |  |
| Total for internal installation Carried to Summary of Cost (Excl.VAT) |  |

| Item | Description | Unit | Quantity | Rate | Amount |
| --- | --- | --- | --- | --- | --- |
|  | Sub Total Brought Forward |  |  |  |  |
| 8 | Demolitions and Alterations |  |  |  |  |
|  | The contractor shall carry out the whole of the works with as little mess and noise as possible and with a minimum of disturbance to adjoining premises and their tenants. He shall provide proper protection and provide, erect and remove when directed, any temporary tarpaulins that may be necessary during the progress of the works, all to the satisfaction of the principal agent. Water supply pipes and other piping that may be encountered and found necessary to disconnect or cut, shall be effectually stopped off or grubbed up and removed, and any new connections that may be necessary shall be made with proper fittings, to the satisfaction of the principal agent |  |  |  |  |
| 8.1 | Removal of the existing light fittings to be stored at GPAA Store room |  |  |  |  |
| 8.2 | Removal of fire detectors, cameras and other items on the ceilings and placing them back after completion |  |  |  |  |
| 8.3 | Make neat to all damages on walls and other items during the alterations Other (specify) |  |  |  |  |
| Total for Alterations Carried to Summary of Cost (Excl.VAT) |  |

Required by:					………………………………….

At:						………………………………….

Brand and model					………………………………….

Country of origin					………………………………….

Does offer comply with specification?			*YES/NO

If not to specification, indicate deviation(s)		………………………………….

Period required for delivery			………………………………….

*Delivery: 						*FIRM/NOT FIRM

Delivery basis					………………………………….

Note:	All delivery costs must be included in the bid price, for delivery at the prescribed destination.

* Delete if not applicable

| ITEM | DESCRIPTION | AMOUNT |
| --- | --- | --- |
| 1 | Preliminary and General |  |
| 2 | Block C First Floor |  |
| 3 | Block D2 |  |
| 4 | Block E204 |  |
| 5 | Block H Basement |  |
| 6 | Block D Lower Ground |  |
|  | Subtotal A |  |
|  | 14 % VAT |  |
| Total VAT inclusive |  |

SBD4

DECLARATION OF INTEREST

- Any legal person, including persons employed by the GPAA, or persons having a kinship with persons employed by GPAA, including a blood relationship, may not make an offer or offers in terms of this invitation to bid.  In view of possible allegations of favouritism, should the resulting bid, or part thereof, be awarded to persons employed by the GPAA, or to persons connected with or related to them, it is required that the bidder or his/her authorised representative declare his/her position in relation to the evaluating/adjudicating committee and/or take an oath declaring his/her interest, where:

  - the bidder is employed by the GPAA; and/or

  - the legal person on whose behalf the bidding document is signed, has a relationship with persons/a person who are/is involved in the evaluation and or adjudication of the bid(s), or where it is known that such a relationship exists between the person or persons for or on whose behalf the declarant acts and persons who are involved with the evaluation and or adjudication of the bid.

- In order to give effect to the above, the following questionnaire must be completed and submitted with the bid.

  - Are you or any person connected with the bidder, employed by GPAA?

    - If so, state particulars:

………………………………………………………………

………………………………………………………………

  - Do you, or any person connected with the bidder, have any relationship (family, friend, other) with a person employed by GPAA and who may be involved with the evaluation and or adjudication of this bid?

    - If so, state particulars:

………………………………………………………………

………………………………………………………………

3.	In order to give effect to the above, the following questionnaire must be completed and submitted with the bid.

  - Full Name of bidder or his or her representative: ….………………………………………….

  - Identity Number: …………………..………………………………………………………………

  - Position occupied in the Company (director, trustee, shareholder²): ………………………..

  - Company Registration Number: …………………………………………………………..…….

  - Tax Reference Number: ………..……………………………………………………….………

3.6     VAT Registration Number: ……………………………………………………………………....

3.6.1	The names of all directors / trustees / shareholders / members, their individual identity numbers, tax reference numbers and, if applicable, employee / persal numbers must be indicated in paragraph 3 below.

¹“State” means –

(a)  Any national or provincial department, national or provincial public entity or constitutional institution       within the meaning of the Public Finance Management Act, 1999 (Act No. 1 of 1999);

(b)	 Any municipality or municipal entity;

(c)	 Provincial legislature;

(d)   National Assembly or the national Council of provinces; or

(e)	 Parliament.

²”Shareholder” means a person who owns shares in the company and is actively involved in the management of the enterprise or business and exercises control over the enterprise.

3.7 	Are you or any person connected with the bidder		        	YES / NO

presently employed by the state?

    - If so, furnish the following particulars:

Name of person / director / trustee / shareholder/ member: .....………………………………

Name of state institution at which you or the person

connected to the bidder is employed:    ………………….………………………………………

Position occupied in the state institution: ……………….………………………………………

Any other particulars:

………………………………………………………………

………………………………………………………………

………………………………………………………………

    - If you are presently employed by the state, did you obtain		YES / NO

the appropriate authority to undertake remunerative

work outside employment in the public sector?

      - If yes, did you attach proof of such authority to the bid		YES / NO

document?

(Note: Failure to submit proof of such authority, where

applicable, may result in the disqualification of the bid.

      - If no, furnish reasons for non-submission of such proof:

…………………………………………………………………….

…………………………………………………………………….

…………………………………………………………………….

  - Did you or your spouse, or any of the company’s directors / 		YES / NO

trustees / shareholders / members or their spouses conduct

business with the state in the previous twelve months?

    - If so, furnish particulars:

…………………………………………………………………..

…………………………………………………………………..

…………………………………………………………………...

  - Do you, or any person connected with the bidder, have	YES / NO

any relationship (family, friend, other) with a person

employed by the state and who may be involved with

the evaluation and or adjudication of this bid?

2.9.1  If so, furnish particulars.

……………………………………………………………...

…………………………………………………………..….

………………………………………………………………

2.10   Are you, or any person connected with the bidder,			YES/NO

aware of any relationship (family, friend, other) between

any other bidder and any person employed by the state

who may be involved with the evaluation and or adjudication

of this bid?

2.10.1   If so, furnish particulars.

………………………………………………………………

………………………………………………………………

………………………………………………………………

2.11   Do you or any of the directors / trustees / shareholders / members 	YES/NO

of the company have any interest in any other related companies

whether or not they are bidding for this contract?

2.11.1	If so, furnish particulars:

…………………………………………………………………………….

…………………………………………………………………………….

…………………………………………………………………………….

# of directors / trustees / members / shareholders.

| Full Name | Identity Number | Personal Tax Reference Number | State Employee Number / Persal Number |
| --- | --- | --- | --- |

- DECLARATION

I, THE UNDERSIGNED (NAME)………………………………………………………………………

CERTIFY THAT THE INFORMATION FURNISHED IN PARAGRAPHS 2 and 3 ABOVE IS CORRECT.

I ACCEPT THAT THE STATE MAY REJECT THE BID OR ACT AGAINST ME IN TERMS OF PARAGRAPH 23 OF THE GENERAL CONDITIONS OF CONTRACT SHOULD THIS DECLARATION PROVE TO BE FALSE.

…………………………………..	 ..……………………………………………

Signature	                          Date

………………………………….	………………………………………………

Position 	Name of bidder

SBD 6.1

PREFERENCE POINTS CLAIM FORM IN TERMS OF THE PREFERENTIAL PROCUREMENT REGULATIONS 2011

This preference form must form part of all bids invited.  It contains general information and serves as a claim form for preference points for Broad-Based Black Economic Empowerment (B-BBEE) Status Level of Contribution

NB:	BEFORE COMPLETING THIS FORM, BIDDERS MUST STUDY THE GENERAL CONDITIONS, DEFINITIONS AND DIRECTIVES APPLICABLE IN RESPECT OF B-BBEE, AS PRESCRIBED IN THE PREFERENTIAL PROCUREMENT REGULATIONS, 2011.

- GENERAL CONDITIONS

  - The following preference point systems are applicable to all bids:

- the 80/20 system for requirements with a Rand value of up to R1 000 000 (all applicable taxes included); and

- the 90/10 system for requirements with a Rand value above R1 000 000 (all applicable taxes included).

  - The value of this bid is estimated to exceed/not exceed R1 000 000 (all applicable taxes included) and therefore the……………………system shall be applicable.

  - Preference points for this bid shall be awarded for:

- Price; and

- B-BBEE Status Level of Contribution.

1.3.1	The maximum points for this bid are allocated as follows:

POINTS

1.3.1.1	PRICE					…………..

1.3.1.2	B-BBEE STATUS LEVEL OF CONTRIBUTION		…………...

Total points for Price and B-BBEE must not exceed 		100

1.4	Failure on the part of a bidder to fill in and/or to sign this form and submit a B-BBEE Verification Certificate from a Verification Agency  accredited by the South African Accreditation System (SANAS) or a Registered Auditor approved by the Independent Regulatory Board of Auditors (IRBA) or an Accounting Officer as contemplated in the Close Corporation Act (CCA) together with the bid, will be interpreted to mean that preference points for B-BBEE status level of contribution are not claimed.

  - The purchaser reserves the right to require of a bidder, either before a bid is adjudicated or at any time subsequently, to substantiate any claim in regard to preferences, in any manner required by the purchaser.

2.	DEFINITIONS

2..1	“all applicable taxes” includes value-added tax, pay as you earn, income tax, unemployment  insurance fund contributions and skills development levies;

2.2	“B-BBEE” means broad-based black economic empowerment as defined in section 1 of the Broad

-Based Black Economic Empowerment Act;

2.3	“B-BBEE status level of contributor” means the B-BBEE status received by a measured entity  based on its overall performance using the relevant scorecard contained in the Codes of Good Practice on Black Economic Empowerment, issued in terms of section 9(1) of the Broad-Based Black Economic Empowerment Act;

2.4	“bid” means a written offer in a prescribed or stipulated form in response to an invitation by

an organ of state for the provision of services, works or goods, through price quotations, advertised competitive bidding processes or proposals;

2.5	“Broad-Based Black Economic Empowerment Act” means the Broad-Based Black Economic Empowerment Act, 2003 (Act No. 53 of 2003);

2.6	“comparative price” means the price after the factors of a non-firm price and all unconditional discounts that can be utilized have been taken into consideration;

2.7	“consortium or joint venture” means an association of persons for the purpose of combining their expertise, property, capital, efforts, skill and knowledge in an activity for the execution of a contract;

2.8	“contract” means the agreement that results from the acceptance of a bid by an organ of

State;

2.9	“EME” means any enterprise with an annual total revenue of R5 million or less.

2.10	“Firm price” means the price that is only subject to adjustments in accordance with the actual increase or decrease resulting from the change, imposition, or abolition of customs or excise duty and any other duty, levy, or tax, which, in terms of the law or regulation, is binding on the contractor and demonstrably has an influence on the price of any supplies, or the rendering costs of any service, for the execution of the contract;

2.11	“functionality” means the measurement according to predetermined norms, as set out in the bid documents, of a service or commodity that is designed to be practical and useful, working or operating, taking into account, among other factors, the quality, reliability, viability and durability of a  service and the technical capacity and ability of a bidder;

2.12	“non-firm prices” means all prices other than “firm” prices;

2.13	“person” includes a juristic person;

2.14	“rand value” means the total estimated value of a contract in South African currency, calculated at  the time of bid invitations, and includes all applicable taxes and excise duties;

2.15    “sub-contract” means the primary contractor’s assigning, leasing, making out work to, or employing, another person to support such primary contractor in the execution of part of a project in terms of the contract;

2.16	“total revenue” bears the same meaning assigned to this expression in the Codes of Good

Practice on Black Economic Empowerment, issued in terms of section 9(1) of the Broad-Based Black Economic Empowerment Act and promulgated in the Government Gazette on 9 February 2007;

2.17	“trust” means the arrangement through which the property of one person is made over or

Bequeathed to a trustee to administer such property for the benefit of another person; and

2.18	“trustee” means any person, including the founder of a trust, to whom property is bequeathed in

order for such property to be administered for the benefit of another person.

3.	ADJUDICATION USING A POINT SYSTEM

3.1	The bidder obtaining the highest number of total points will be awarded the contract.

3.2	Preference points shall be calculated after prices have been brought to a comparative basis taking into account all factors of non-firm prices and all unconditional discounts;.

3.3	Points scored must be rounded off to the nearest 2 decimal places.

3.4        In the event that two or more bids have scored equal total points, the successful bid must be the one scoring the highest number of preference points for B-BBEE.

3.5        However, when functionality is part of the evaluation process and two or more bids have scored equal points including equal preference points for B-BBEE, the successful bid must be the one scoring the highest score for functionality.

  - Should two or more bids be equal in all respects, the award shall be decided by the drawing of lots.

4.	POINTS AWARDED FOR PRICE

4.1	THE 80/20 OR 90/10 PREFERENCE POINT SYSTEMS

A maximum of 80 or 90 points is allocated for price on the following basis:

# 80/20	or	90/10

Or

Where

Ps	=	Points scored for comparative price of bid under consideration

Pt	=	Comparative price of bid under consideration

Pmin	=	Comparative price of lowest acceptable bid

- Points awarded for B-BBEE Status Level of Contribution

5.1	In terms of Regulation 5 (2) and 6 (2) of the Preferential Procurement Regulations, preference points must be awarded to a bidder for attaining the B-BBEE status level of contribution in accordance with the table below:

| B-BBEE Status Level of Contributor | Number of points (90/10 system) | Number of points (80/20 system) |
| --- | --- | --- |
| 1 | 10 | 20 |
| 2 | 9 | 18 |
| 3 | 8 | 16 |
| 4 | 5 | 12 |
| 5 | 4 | 8 |
| 6 | 3 | 6 |
| 7 | 2 | 4 |
| 8 | 1 | 2 |
| Non-compliant contributor | 0 | 0 |

5.2	Bidders who qualify as EMEs in terms of the B-BBEE Act must submit a certificate issued by an Accounting Officer as contemplated in the CCA or a Verification Agency accredited by SANAS or a Registered Auditor.  Registered auditors do not need to meet the prerequisite for IRBA’s approval for the purpose of conducting verification and issuing EMEs with B-BBEE Status Level Certificates.

5.3	Bidders other than EMEs must submit their original and valid B-BBEE status level verification certificate or a certified copy thereof, substantiating their B-BBEE rating issued by a Registered Auditor approved by IRBA or a Verification Agency accredited by SANAS.

5.4       A trust, consortium or joint venture, will qualify for points for their B-BBEE status level as a

legal entity provided that the entity submits their B-BBEE status level certificate.

5.5       A trust, consortium or joint venture will qualify for points for their B-BBEE status level as an

Unincorporated entity, provided that the entity submits their consolidated B-BBEE scorecard as if they were a group structure and that such a consolidated B-BBEE scorecard is prepared for every separate bid.

5.6       Tertiary institutions and public entities will be required to submit their B-BBEE status level

Certificates in terms of the specialized scorecard contained in the B-BBEE Codes of Good

Practice.

5.7        A person will not be awarded points for B-BBEE status level if it is indicated in the bid

documents that such a bidder intends sub-contracting more than 25% of the value of the

Contract to any other enterprise that does not qualify for at least the points that such a bidder qualifies for, unless the intended sub-contractor is an EME that has the capability and ability to execute the sub-contract.

5.8        A person awarded a contract may not sub-contract more than 25% of the value of the contract to any other enterprise that does not have an equal or higher B-BBEE status level than the person concerned, unless the contract is sub-contracted to an EME that has the capability and ability to execute the sub-contract.

6.	 BID DECLARATION

  - Bidders who claim points in respect of B-BBEE Status Level of Contribution must complete the

Following:

7.       	B-BBEE STATUS LEVEL OF CONTRIBUTION CLAIMED IN TERMS OF PARAGRAPHS

1.3.1.2 AND 5.1

7.1   B-BBEE Status Level of Contribution:  ………...….      =     ……….… (Maximum of 10 or 20

points)

(Points claimed in respect of paragraph 7.1 must be in accordance with the table reflected in paragraph  5.1 and must be substantiated by means of a B-BBEE certificate issued by a Verification Agency accredited by SANAS or a Registered Auditor approved by IRBA or an Accounting Officer as contemplated in the CCA).

8	SUB-CONTRACTING

8.1     	Will any portion of the contract be sub-contracted?     YES / NO (delete which is not applicable)

8.1.1	If yes, indicate:

(i) 	What percentage of the contract will be subcontracted?	............……………….…%

(ii) 	The name of the sub-contractor?	…………………………………………………………..

(iii) 	The B-BBEE status level of the sub-contractor?	…….………………..

(iv)	Whether the sub-contractor is an EME?		YES / NO (delete which is not

applicable)

9	DECLARATION WITH REGARD TO COMPANY/FIRM

9.1	Name of company/firm

9.2	VAT registration number		:

9.3	Company registration number		…………………………………………………………………….					:

9.4	TYPE OF COMPANY/ FIRM

(	Partnership/Joint Venture / Consortium

(	One person business/sole propriety

(	Close corporation

(	Company

(	(Pty) Limited

[Tick applicable box]

9.5	DESCRIBE PRINCIPAL BUSINESS ACTIVITIES

…………..

………………

……………..

9.6	COMPANY CLASSIFICATION

(	Manufacturer

(	Supplier

(	Professional service provider

(	Other service providers, e.g. transporter, etc.

[Tick applicable box]

9.7	Total number of years the company/firm has been in business? ……………………………………

9.8	I/we, the undersigned, who is / are duly authorised to do so on behalf of the company/firm, certify that the points claimed, based on the B-BBE status level of contribution indicated in paragraph 7 of the foregoing certificate, qualifies the company/ firm for the preference(s) shown and I / we acknowledge that:

(i)	The information furnished is true and correct;

(ii)	The preference points claimed are in accordance with the General Conditions as indicated in paragraph 1 of this form.

(iii)	In the event of a contract being awarded as a result of points claimed as shown in paragraph 7, the contractor may be required to furnish documentary proof to the satisfaction of the purchaser that the claims are correct;

(iv)	If the B-BBEE status level of contribution has been claimed or obtained on a fraudulent basis or any of the conditions of contract have not been fulfilled, the purchaser may, in addition to any other remedy it may have –

(a)	Disqualify the person from the bidding process;

(b)	Recover costs, losses or damages it has incurred or suffered as a result of that person’s conduct;

(c)	Cancel the contract and claim any damages which it has suffered as a result of having to make less favourable arrangements due to such cancellation;

- restrict the bidder or contractor, its shareholders and directors, or only the shareholders and directors who acted on a fraudulent basis, from obtaining business from any organ of state for a period not exceeding 10 years, after the audi alter am partem (hear the other side) rule has been applied; and

- forward the matter for criminal prosecution

WITNESSES:

- ………………………………………

..…………………………..………

SIGNATURE(S) OF BIDDER(S)

- ………………………………………

DATE:…………………………..……..

ADDRESS:…………………………..

..…………………..…..…………						                                                                          …………………………...

….…………………..…..

…………………………..

SBD8

DECLARATION OF BIDDER’S PAST SUPPLY CHAIN MANAGEMENT PRACTICES

- This Standard Bidding Document must form part of all bids invited.

- It serves as a declaration to be used by institutions in ensuring that when goods and services are being procured, all reasonable steps are taken to combat the abuse of the supply chain management system.

- The bid of any bidder may be disregarded if that bidder, or any of its directors have:

- abused the institution’s supply chain management system;

- committed fraud or any other improper conduct in relation to such system; or

- Failed to perform on any previous contract.

- In order to give effect to the above, the following questionnaire must be completed and submitted with the bid.

| Item | Question | Yes | No |
| --- | --- | --- | --- |
| 4.1 | Is the bidder or any of its directors listed on the National Treasury’s database as companies or persons prohibited from doing business with the public sector? (Companies or persons who are listed on this database were informed in writing of this restriction by the National Treasury after the Audi alter am partem rule was applied). | Yes | No |
| 4.1.1 | If so, furnish particulars: |
| 4.2 | Is the bidder or any of its directors listed on the Register for Tender Defaulters in terms of section 29 of the Prevention and Combating of Corrupt Activities Act (No 12 of 2004)? To access this Register enter the National Treasury’s website, www.treasury.gov.za, click on the icon “Register for Tender Defaulters” or submit your written request for a hard copy of the Register to facsimile number (012) 3265445. | Yes | No |
| 4.2.1 | If so, furnish particulars: |
| 4.3 | Was the bidder or any of its directors convicted by a court of law (including a court outside of the Republic of South Africa) for fraud or corruption during the past five years? | Yes | No |
| 4.3.1 | If so, furnish particulars: |
| 4.4 | Was any contract between the bidder and any organ of state terminated during the past five years on account of failure to perform on or comply with the contract? | Yes | No |
| 4.4.1 | If so, furnish particulars: |

CERTIFICATION

I, THE UNDERSIGNED (FULL NAME)………………………… CERTIFY THAT THE INFORMATION FURNISHED ON THIS DECLARATION FORM IS TRUE AND CORRECT.

I ACCEPT THAT, IN ADDITION TO CANCELLATION OF A CONTRACT, ACTION MAY BE TAKEN AGAINST ME SHOULD THIS DECLARATION PROVE TO BE FALSE.

………………………………………...			…………………………………..

Signature 		Date

………………………………………...			…………………………………..

Position 		Name of Bidder

SBD 9

CERTIFICATE OF INDEPENDENT BID DETERMINATION

1	This Standard Bidding Document (SBD) must form part of all bids¹ invited.

2	Section 4 (1) (b) (iii) of the Competition Act No. 89 of 1998, as amended, prohibits an agreement between, or concerted practice by, firms, or a decision by an association of firms, if it is between parties in a horizontal relationship and if it involves collusive bidding (or bid rigging).² Collusive bidding is a pe se prohibition meaning that it cannot be justified under any grounds.

3	Treasury Regulation 16A9 prescribes that accounting officers and accounting authorities must take all reasonable steps to prevent abuse of the supply chain management system and authorizes accounting officers and accounting authorities to:

a.	disregard the bid of any bidder if that bidder, or any of its directors have abused the institution’s supply chain management system and or committed fraud or any other improper conduct in relation to such system.

b.	cancel a contract awarded to a supplier of goods and services if the supplier committed any corrupt or fraudulent act during the bidding process or the execution of that contract.

- This SBD serves as a certificate of declaration that would be used by institutions to ensure that, when bids are considered, reasonable steps are taken to prevent any form of bid-rigging.

- In order to give effect to the above, the attached Certificate of Bid Determination (SBD 9) must be completed and submitted with the bid:

¹ Includes price quotations, advertised competitive bids, limited bids and proposals.

² Bid rigging (or collusive bidding) occurs when businesses, that would otherwise be expected to compete, secretly conspire to raise prices or lower the quality of goods and / or services for purchasers who wish to acquire goods and / or services through a bidding process.  Bid rigging is, therefore, an agreement between competitors not to compete.

SBD 9

CERTIFICATE OF INDEPENDENT BID DETERMINATION

I, the undersigned, in submitting the accompanying bid:

________________________________________________________________________

(Bid Number and Description)

in response to the invitation for the bid made by:

________________________________________________________________________

(Name of Institution)

Do hereby make the following statements that I certify to be true and complete in every respect:

I certify, on behalf of: _______________________________________________that:

(Name of Bidder)

- I have read and I understand the contents of this Certificate;

- I understand that the accompanying bid will be disqualified if this Certificate is found not to be true and complete in every respect;

- I am authorized by the bidder to sign this Certificate, and to submit the accompanying bid, on behalf of the bidder;

- Each person whose signature appears on the accompanying bid has been authorized by the bidder to determine the terms of, and to sign the bid, on behalf of the bidder;

- For the purposes of this Certificate and the accompanying bid, I understand that the word “competitor” shall include any individual or organization, other than the bidder, whether or not affiliated with the bidder, who:

    - has been requested to submit a bid in response to this bid invitation;

(b) 	Could potentially submit a bid in response to this bid invitation, based on their qualifications, abilities or experience; and

(c)	Provides the same goods and services as the bidder and/or is in the same line of business as the bidder

- The bidder has arrived at the accompanying bid independently from, and without consultation, communication, agreement or arrangement with any competitor. However communication between partners in a joint venture or consortium³ will not be construed as collusive bidding.

- In particular, without limiting the generality of paragraphs 6 above, there has been no consultation, communication, agreement or arrangement with any competitor regarding:

- prices;

- geographical area where product or service will be rendered (market allocation)

(c) 	Methods, factors or formulas used to calculate prices;

(d)	The intention or decision to submit or not to submit, a bid;

(e)	The submission of a bid which does not meet the specifications and conditions of the bid; or

(f)         Bidding with the intention not to win the bid.

- In addition, there have been no consultations, communications, agreements or arrangements with any competitor regarding the quality, quantity, specifications and conditions or delivery particulars of the products or services to which this bid invitation relates.

- The terms of the accompanying bid have not been, and will not be, disclosed by the bidder, directly or indirectly, to any competitor, prior to the date and time of the official bid opening or of the awarding of the contract.

³ Joint venture or Consortium means an association of persons for the purpose of combining their expertise, property, capital, efforts, skill and knowledge in an activity for the execution of a contract.

- I am aware that, in addition and without prejudice to any other remedy provided to combat any restrictive practices related to bids and contracts, bids that are suspicious will be reported to the Competition Commission for investigation and possible imposition of administrative penalties in terms of section 59 of the Competition Act No 89 of 1998 and or may be reported to the National Prosecuting Authority (NPA) for criminal investigation and or may be restricted from conducting business with the public sector for a period not exceeding ten (10) years in terms of the Prevention and Combating of Corrupt Activities Act No 12 of 2004 or any other applicable legislation.

……………………………………………..     …………………………………..

Name of Bidder				     Signature

……………………………………                   …………………………………

Position 					       Date

## Special Conditions of Contract

General Notes

The purpose of this Special Conditions of Contract (SCC) is to: Draw special attention to certain special conditions applicable to Bids, Contracts, Agreements and Orders of the Government Employee Pension Fund (GPAA); and (ii) To ensure that all bidders are familiar with the special provisions, requirements and conditions that will be applicable in the undertaking of the project and which will form part of the contract documentation and of which due cognisance must be taken in the bidding process. In this document words in the singular also mean in the plural and vice versa and words in the masculine also mean in the feminine and neuter. The General Conditions of Contract (GCC) also forms part of all bidding documents and must be read in conjunction with this Special Conditions of Contract. Whenever there is a conflict between the GCC and the SCC, the provisions in the SCC shall prevail.

  - Bid Submission

    - Bidders will be permitted to submit bids by:

Hand: 34 Hamilton Street, Arcadia, Pretoria

    - Closing Date:    07 April 2017

    - Closing time: 11:00 am.

    - Compulsory briefing session will held on 24 March 2017    at 34 Hamilton Street, Arcadia, Pretoria at 10h00 am.

  - Validity of Bids

    - Bidders are required to submit bids valid for 120 days.

  - Two-stage Bidding

    - For this bid, a two-stage bidding procedure will be used, under which first un-priced

technical proposals on the basis of a conceptual design or performance specifications are invited. The price proposal will only be considered after the technical proposal has been confirmed as being competent and compliant.

    - Suppliers are requested to submit their proposal in separate envelopes, with the technical 	proposal separated         from the price proposal.

    - A minimum number of five (5) copies of the technical proposal are required as well as

Five (5) copies of the pricing proposal in a separate envelope.

    - Only suppliers who meet the minimum of 60% on functionality will be considered

for second stage of evaluation.

1.3.6	Government Pension Administration Agency (GPAA) reserve the right to increase or decrease the number of suppliers awarded based on decision deem fit and the workload to be carried out.

  - Late Bids

1.4.1	Bids received after the time stipulated will not be considered. Late bids will be posted back to the bidder un-opened.

  - Clarification or Alterations of Bids

    - Bidders will not be requested or permitted to alter their bids after the deadline for receipt of bids.

    - Requests for clarification needed to evaluate bids and the bidder’s responses should be made in writing.

  - Administrative requirements

If a bid is not substantially responsive, that is, it contains material deviations from or reservations to the terms, conditions and specifications in the bidding documents, it will not be considered further.

    - It will be ascertained whether bids:

- Include original tax clearance certificates/ SARS pin;

- Include compulsory SBD forms that have been properly signed and completed (SBD 3.1; SBD4; SBD 6.1; SBD 8 and SBD 9);

- Include a technical proposal / response;

- Each price item must be completed.

(Refer to Administrative Compliance of Evaluation Criteria)

    - The bidder will not be permitted to correct or withdraw material deviations or reservations once bids have

been opened.

1.6.3	 GPAA reserve the right to add and remove refreshments and consumables listed and not listed.

  - Rejection of all Bids

GPAA reserves the right to reject of all bids if and when deemed necessary. This is justified when there is lack of effective competition, or bids are not substantially responsive.

  - Associations between Consultants

    - Consultants are encouraged to associate with each other to complement their     empowerment 	credentials and their respective areas of expertise, or for other reasons. Such an association may be for the long term (independent of any particular assignment) or for a specific assignment. The association may take the form of a joint venture or a sub consultancy.

    - Consultants who do form a joint venture will agree on their terms and conditions and inform the GPAA of    the details of such a joint venture for approval.

1.9    	Bidder Selection

1.9.1             The GPAA reserves the right to select the appropriate bidders based on its requirements, and

The decision of the adjudication panel and the CEO of GPAA will be considered final.

1.10		Project team to service GPAA

Note that if changes are made to the Project team proposed in the tender after the bid has           been awarded, this has to be cleared with GPAA first.

  - Companies must also submit copy of ID of shareholders and bank letter.

  - Companies will be subjected to risk assessment prior to award.

Annexure C

(GPAA)

SCM

General Conditions of Contract

GPAA PROCUREMENT:  GENERAL CONDITIONS OF CONTRACT

The purpose of this Annexure is to:

- Draw special attention to certain general conditions applicable to GPAA bids, contracts and orders; and

- To ensure that clients be familiar with regard to the rights and obligations of all parties involved in doing business with GPAA.

  - In this document words in the singular also mean in the plural and vice versa and words in the masculine also mean in the feminine and neuter.

  - The General Conditions of Contract will form part of all bid documents and may not be amended.

  - Special Conditions of Contract (SCC) relevant to a specific bid should be compiled separately for every bid if applicable and will supplement the General Conditions of Contract. Whenever there is a conflict, the provisions in the SCC shall prevail.

TABLE OF CLAUSES

- Definitions

- Application

- General

- Standards

- Use of contract documents and information; inspection

- Patent rights

- Performance security

- Inspections, tests and analysis

- Packing

- Delivery and documents

- Insurance

- Transportation

- Incidental services

- Spare parts

- Warranty

- Payment

- Prices

- Contract amendments

- Assignment

- Subcontracts

- Delays in the supplier’s performance

- Penalties

- Termination for default

- Dumping and countervailing duties

- Force Majeure

- Termination for insolvency

- Settlement of disputes

- Limitation of liability

- Governing language

- Applicable law

- Notices

- Taxes and duties

- DEFINITIONS

The following terms shall be interpreted as indicated:

  - “Closing time” means the date and hour specified in the bidding documents for the receipt of bids.

  - “Contract” means the written agreement entered into between the purchaser and the supplier, as recorded in the contract form signed by the parties, including all attachments and appendices thereto and all documents incorporated by reference therein.

  - “Contract price” means the price payable to the supplier under the contract for the full and proper performance of his contractual obligations.

  - “Corrupt practice” means the offering, giving, receiving, or soliciting of anything of value to influence the action of a public employee in the procurement process or in contract execution.

  - "Countervailing duties" are imposed in cases where an enterprise abroad is subsidized by its GPAA and encouraged to market its products internationally.

  - “Country of origin” means the place where the goods were mined, grown or produced or from which the services are supplied. Goods are produced when, through manufacturing, processing or substantial and major assembly of components, a commercially recognized new product results that is substantially different in basic characteristics or in purpose or utility from its components.

  - “Day” means calendar day.

  - “Delivery” means delivery in compliance of the conditions of the contract or order.

  - “Delivery ex stock” means immediate delivery directly from stock actually on hand.

  - “Delivery into consignees store or to his site” means delivered and unloaded in the specified store or depot or on the specified site in compliance with the conditions of the contract or order, the supplier bearing all risks and charges involved until the supplies are so delivered and a valid receipt is obtained.

  - "Dumping" occurs when a private enterprise abroad market its goods on own initiative in the RSA at lower prices than that of the country of origin and which have the potential to harm the local industries in the RSA.

  - ”Force majeure” means an event beyond the control of the supplier and not involving the supplier’s fault or negligence and not foreseeable. Such events may include, but is not restricted to, acts of the purchaser in its sovereign capacity, wars or revolutions, fires, floods, epidemics, quarantine restrictions and freight embargoes.

  - “Fraudulent practice” means a misrepresentation of facts in order to influence a procurement process or the execution of a contract to the detriment of any bidder, and includes collusive practice among bidders (prior to or after bid submission) designed to establish bid prices at artificial non-competitive levels and to deprive the bidder of the benefits of free and open competition.

  - “GCC” mean the General Conditions of Contract.

  - “Goods” means all of the equipment, machinery, and/or other materials that the supplier is required to supply to the purchaser under the contract

  - “Imported content” means that portion of the bidding price represented by the cost of components, parts or materials which have been or are still to be imported (whether by the supplier or his subcontractors) and which costs are inclusive of the costs abroad, plus freight and other direct importation costs such as landing costs, dock dues, import duty, sales duty or other similar tax or duty at the South African place of entry as well as transportation and handling charges to the factory in the Republic where the supplies covered by the bid will be manufactured.

  - “Local content” means that portion of the bidding price which is not included in the imported content provided that local manufacture does take place.

  - “Manufacture” means the production of products in a factory using labour, materials, components and machinery and includes other related value-adding activities.

  - “Order” means an employee written order issued for the supply of goods for works or the rendering of a service.

  - “Project site,” where applicable, means the place indicated in bidding documents.

  - “Purchaser” means the organization purchasing the goods.

  - “Republic” means the Republic of South Africa.

  - “SCC” means the Special Conditions of Contract.

  - “Services” means those functional services ancillary to the supply of the goods, such as transportation and any other incidental services, such as installation, commissioning, provision of technical assistance, training, catering, gardening, security, maintenance and other such obligations of the supplier covered under the contract.

  - “Written” or “in writing” means handwritten in ink or any form of 96 electronic or mechanical writing.

- APPLICATION

  - These general conditions are applicable to all bids, contracts and orders including bids for functional and professional services, sales, hiring, letting and the granting or acquiring of rights, but excluding immovable property, unless otherwise indicated in the bidding documents.

  - Where applicable, special conditions of contract are also laid down to cover specific supplies, services or works.

  - Where such special conditions of contract are in conflict with these general conditions, the special conditions shall apply.

- GENERAL

  - Unless otherwise indicated in the bidding documents, the purchaser shall not be liable for any expense incurred in the preparation and submission of a bid. Where applicable a non-refundable fee for documents may be charged.

  - With certain exceptions, invitations to bid are only published in the State Tender Bulletin. The State Tender Bulletin may be obtained directly from the Government Printer, Private Bag X85, Pretoria 0001, or accessed electronically from www.employee.gov.za.

- STANDARDS

  - The goods supplied shall conform to the standards mentioned in the bidding documents and specifications.

- USE OF CONTRACT DOCUMENTS AND INFORMATION; INSPECTION

  - The supplier shall not, without the purchaser’s prior written consent, disclose the contract, or any provision thereof, or any specification, plan, drawing, pattern, sample, or information furnished by or on behalf of the purchaser in connection therewith, to any person other than a person employed by the supplier in the performance of the contract. Disclosure to any such employed person shall be made in confidence and shall extend only so far as may be necessary for purposes of such performance.

  - The supplier shall not, without the purchaser’s prior written consent, make use of any document or information mentioned in GCC clause 5.1 except for purposes of performing the contract.

  - Any document, other than the contract itself mentioned in GCC clause 5.1 shall remain the property of the purchaser and shall be returned (all copies) to the purchaser on completion of the supplier’s performance under the contract if so required by the purchaser.

  - The supplier shall permit the purchaser to inspect the supplier’s records relating to the performance of the supplier and to have them audited by auditors appointed by the purchaser, if so required by the purchaser.

- PATENT RIGHTS

  - The supplier shall indemnify the purchaser against all third-party claims of infringement of patent, trademark, or industrial design rights arising from use of the goods or any part thereof by the purchaser.

- PERFORMANCE

  - Within thirty (30) days of receipt of the notification of contract award, the successful bidder shall furnish to the purchaser the performance security of the amount specified in SCC.

  - The proceeds of the performance security shall be payable to the purchaser as compensation for any loss resulting from the supplier’s failure to complete his obligations under the contract.

  - The performance security shall be denominated in the currency of the contract, or in a freely convertible currency acceptable to the purchaser and shall be in one of the following forms:

    - a bank guarantee or an irrevocable letter of credit issued by a reputable bank located in the purchaser’s country or abroad, acceptable to the purchaser, in the form provided in the bidding documents or another form acceptable to the purchaser; or

    - a cashier’s or certified cheque

  - The performance security will be discharged by the purchaser and returned to the supplier not later than thirty (30) days following the date of completion of the supplier’s performance obligations under the contract, including any warranty obligations, unless otherwise specified in SCC.

- INSPECTIONS, TESTS AND ANALYSES

  - All pre-bidding testing will be for the account of the bidder.

  - If it is a bid condition that supplies to be produced or services to be rendered should at any stage during production or execution or on completion be subject to inspection, the premises of the bidder or contractor shall be open, at all reasonable hours, for inspection by a representative of the Department or an organization acting on behalf of the Department.

  - If there is no inspection requirements indicated in the bidding documents and no mention is made in the contract, but during the contract period it is decided that inspections shall be carried out, the purchaser shall itself make the necessary arrangements, including payment arrangements with the testing Energy Board concerned.

  - If the inspections, tests and analyses referred to in clauses 8.2 and 8.3 show the supplies to be in accordance with the contract requirements, the cost of the  inspections, tests and analyses shall be defrayed by the purchaser.

  - Where the supplies or services referred to in clauses 8.2 and 8.3 do not comply with the contract requirements, irrespective of whether such supplies or services are accepted or not, the cost in connection with these inspections, tests or analyses shall be defrayed by the supplier.

Supplies and services which are referred to in clauses 8.2 and 8.3 and which do not comply with the contract requirements may be rejected.

Any contract supplies may on or after delivery be inspected, tested or analyzed and may be rejected if found not to comply with the requirements of the contract. Such rejected supplies shall be held at the cost and risk of the supplier who shall, when called upon, remove them immediately at his own cost and forthwith substitute them with supplies which do comply with the requirements of the contract. Failing such removal the rejected supplies shall be returned at the suppliers cost and risk. Should the supplier fail to provide the substitute supplies forthwith, the purchaser may, without giving the supplier further opportunity to substitute the rejected supplies, purchase such supplies as may be necessary at the expense of the supplier.

The provisions of clauses 8.4 to 8.7 shall not prejudice the right of the purchaser to cancel the contract on account of a breach of the conditions thereof, or to act in terms of Clause 23 of GCC.

- PACKING

The supplier shall provide such packing of the goods as is required to prevent their damage or deterioration during transit to their final destination, as indicated in the contract. The packing shall be sufficient to withstand, without limitation, rough handling during transit and exposure to extreme temperatures, salt and precipitation during transit, and open storage. Packing, case size and weights shall take into consideration, where appropriate, the remoteness of the goods’ final destination and the absence of heavy handling facilities at all points in transit.

The packing, marking, and documentation within and outside the packages shall comply strictly with such special requirements as shall be expressly provided for in the contract, including additional requirements, if any, specified in SCC, and in any subsequent instructions ordered by the purchaser.

- DELIVERY OF DOCUMENTS

Delivery of the goods shall be made by the supplier in accordance with the terms specified in the contract. The details of shipping and/or other documents to be furnished by the supplier are specified in SCC.

  - Documents to be submitted by the supplier are specified in SCC.

- INSURANCE

The goods supplied under the contract shall be fully insured in a freely convertible currency against loss or damage incidental to manufacture or acquisition, transportation, storage and delivery in the manner specified in the SCC.

- TRANSPORTATION

  - Should a price other than an all-inclusive delivered price be required, this shall be specified in the SCC.

- INCIDENTAL SERVICES

The supplier may be required to provide any or all of the following services, including additional services, if any, specified in SCC:

- performance or supervision of on-site assembly and/or commissioning of the supplied goods;

- furnishing of tools required for assembly and/or maintenance of the supplied goods;

- furnishing of a detailed operations and maintenance manual for each appropriate unit of the supplied goods;

- performance or supervision or maintenance and/or repair of the supplied goods, for a period of time agreed by the parties, provided that this service shall not relieve the supplier of any warranty obligations under this contract; and

- Training of the purchaser’s personnel, at the supplier’s plant and/or on-site, in assembly, start-up, operation, maintenance, and/or repair of the supplied goods.

  - Prices charged by the supplier for incidental services, if not included in the contract price for the goods, shall be agreed upon in advance by the parties and shall not exceed the prevailing rates charged to other parties by the supplier for similar services.

- SPARE PARTS

As specified in SCC, the supplier may be required to provide any or all of the following materials, notifications, and information pertaining to spare parts manufactured or distributed by the supplier:

- such spare parts as the purchaser may elect to purchase from the supplier, provided that this election shall not relieve the supplier of any warranty obligations under the contract; and

- in the event of termination of production of the spare parts:

- Advance notification to the purchaser of the pending termination, in sufficient time to permit the purchaser to procure needed requirements; and

- Following such termination, furnishing at no cost to the purchaser, the blueprints, drawings, and specifications of the spare parts, if requested.

- WARRANTY

  - The supplier warrants that the goods supplied under the contract are new, unused, of the most recent or current models, and that they incorporate all recent improvements in design and materials unless provided otherwise in the contract. The supplier further warrants that all goods supplied under this contract shall have no defect, arising from design, materials, or workmanship (except when the design and/or material is required by the purchaser’s specifications) or from any act or omission of the supplier, that may develop under normal use of the supplied goods in the conditions prevailing in the country of final destination.

  - This warranty shall remain valid for twelve (12) months after the goods, or any portion thereof as the case may be, have been delivered to and accepted at the final destination indicated in the contract, or for eighteen (18) months after the date of shipment from the port or place of loading in the source country, whichever period concludes earlier, unless specified otherwise in SCC.

  - The purchaser shall promptly notify the supplier in writing of any claims arising under this warranty.

  - Upon receipt of such notice, the supplier shall, within the period specified in SCC and with all reasonable speed, repair or replace the defective goods or parts thereof, without costs to the purchaser.

  - Upon receipt of such notice, the supplier shall, within the period specified in SCC and with all reasonable speed, repair or replace the defective goods or parts thereof, without costs to the purchaser.

  - If the supplier, having been notified, fails to remedy the defect(s) within the period specified in SCC, the purchaser may proceed to take such remedial action as may be necessary, at the supplier’s risk and expense and without prejudice to any other rights which the purchaser may have against the supplier under the contract.

- PAYMENT

  - The method and conditions of payment to be made to the supplier under this contract shall be specified in SCC.

  - The supplier shall furnish the purchaser with an invoice accompanied by a copy of the delivery note and upon fulfilment of other obligations stipulated in the contract.

  - Payments shall be made promptly by the purchaser, but in no case later than thirty (30) days after submission of an invoice or claim by the supplier.

  - Payment will be made in Rand unless otherwise stipulated in SCC.

- PRICES

  - Prices charged by the supplier for goods delivered and services performed under the contract shall not vary from the prices quoted by the supplier in his bid, with the exception of any price adjustments authorized in SCC or in the purchaser’s request for bid validity extension, as the case may be.

- CONTRACT AMENDMENTS

  - No variation in or modification of the terms of the contract shall be made except by written amendment signed by the parties concerned.

- ASSIGNMENT

  - The supplier shall not assign, in whole or in part, its obligations to perform under the contract, except with the purchaser’s prior written consent.

- SUBCONTRACTS

  - The supplier shall notify the purchaser in writing of all subcontracts awarded under this contract if not already specified in the bid. Such notification, in the original bid or later, shall not relieve the supplier from any liability or obligation under the contract.

- DELAYS IN THE SUPPLIERS PERFORMANCE

  - Delivery of the goods and performance of services shall be made by the supplier in accordance with the time schedule prescribed by the purchaser in the contract.

  - If at any time during performance of the contract, the supplier or its subcontractor(s) should encounter conditions impeding timely delivery of the goods and performance of services, the supplier shall promptly notify the purchaser in writing of the fact of the delay, it’s likely duration and its cause(s). As soon as practicable after receipt of the supplier’s notice, the purchaser shall evaluate the situation and may at his discretion extend the supplier’s time for performance, with or without the imposition of penalties, in which case the extension shall be ratified by the parties by amendment of contract.

  - No provision in a contract shall be deemed to prohibit the obtaining of supplies or services from a national department, provincial department, or local authorities.

  - The right is reserved to procure outside of the contract small quantities or to have minor essential services executed if an emergency arises, the supplier’s point of supply is not situated at or near the place where the supplies are required, or the supplier’s services are not readily available.

  - Except as provided under GCC Clause 25, a delay by the supplier in the performance of its delivery obligations shall render the supplier liable to the imposition of penalties, pursuant to GCC Clause 22, unless an extension of time is agreed upon pursuant to GCC Clause 21.2 without the application of penalties.

  - Upon any delay beyond the delivery period in the case of supplies contract, the purchaser shall, without cancelling the contract, be entitled to purchase supplies of a similar quality and up to the same quantity in substitution of the goods not supplied in conformity with the contract and to return any goods delivered later at the supplier’s expense and risk, or to cancel the contract and  buy such goods as may be required to complete the contract and without prejudice to his other rights, be entitled to claim damages from the supplier.

- PENALTIES

  - Subject to GCC Clause 25, if the supplier fails to deliver any or all of the goods or to perform the services within the period(s) specified in the contract, the purchaser shall, without prejudice to its other remedies under the contract, deduct from the contract price, as a penalty, a sum calculated on the delivered price of the delayed goods or unperformed services using the current prime interest rate calculated for each day of the delay until actual delivery or performance. The purchaser may also consider termination of the contract pursuant to GCC Clause 23.

- TERMINATION FOR DEFAULT

  - The purchaser, without prejudice to any other remedy for breach of contract, by written notice of default sent to the supplier, may terminate this contract in whole or in part:

- if the supplier fails to deliver any or all of the goods within the period(s) specified in the contract, or within any extension thereof granted by the purchaser pursuant to GCC Clause 21.2;

- if the Supplier fails to perform any other obligation(s) under the contract; or

- If the supplier, in the judgment of the purchaser, has engaged in corrupt or fraudulent practices in competing for or in executing the contract.

  - In the event the purchaser terminates the contract in whole or in part, the purchaser may procure, upon such terms and in such manner as it deems appropriate, goods, works or services similar to those undelivered, and the supplier shall be liable to the purchaser for any excess costs for such similar goods, works or services. However, the supplier shall continue performance of the contract to the extent not terminated.

- ANTI-DUMPING AND COUNTERVAILING DUTIES AND RIGHTS

  - When, after the date of bid, provisional payments are required, or antidumping or countervailing duties are imposed, or the amount of a provisional payment or anti-dumping or countervailing right is increased in respect of any dumped or subsidized import, the State is not liable for any amount so required or imposed, or for the amount of any such increase. When, after the said date, such a provisional payment is no longer required or any such anti-dumping or countervailing right is abolished, or where the amount of such provisional payment or any such right is reduced, any such favourable difference shall on demand be paid forthwith by the contractor to the State or the State may deduct such amounts from moneys (if any) which may otherwise be due to the contractor in regard to supplies or services which he delivered or rendered, or is to deliver or render in terms of the contract or any other contract or any other amount which may be due to him.

- FORCE MAJEURE

Notwithstanding the provisions of GCC Clauses 22 and 23, the supplier shall not be liable for forfeiture of its performance security, damages, or termination for default if and to the extent that his delay in performance or other failure to perform his obligations under the contract is the result of an event of force majeure.

If a force majeure situation arises, the supplier shall promptly notify the purchaser in writing of such condition and the cause thereof. Unless otherwise directed by the purchaser in writing, the supplier shall continue to perform its obligations under the contract as far as is reasonably practical, and shall seek all reasonable alternative means for performance not prevented by the force majeure event.

- TERMINATION FOR INSOLVENCY

The purchaser may at any time terminate the contract by giving written notice to the supplier if the supplier becomes bankrupt or otherwise insolvent. In this event, termination will be without compensation to the supplier, provided that such termination will not prejudice or affect any right of action or remedy which has accrued or will accrue thereafter to the purchaser.

- SETTLEMENT OF DISPUTES

If any dispute or difference of any kind whatsoever arises between the purchaser and the supplier in connection with or arising out of the contract, the parties shall make every effort to resolve amicably such dispute or difference by mutual consultation.

If, after thirty (30) days, the parties have failed to resolve their dispute or difference by such mutual consultation, then either the purchaser or the supplier may give notice to the other party of his intention to commence with mediation. No mediation in respect of this matter may be commenced unless such notice is given to the other party.

Should it not be possible to settle a dispute by means of mediation, it may be settled in a South African court of law.

Mediation proceedings shall be conducted in accordance with the rules of procedure specified in the SCC.

Notwithstanding any reference to mediation and/or court proceedings herein,

- the parties shall continue to perform their respective obligations under the contract unless they otherwise agree; and

- The purchaser shall pay the supplier any monies due the supplier.

Except in cases of criminal negligence or wilful misconduct, and in the case of infringement pursuant to Clause 6.

- LIMITATION OF LIABILITY

The supplier shall not be liable to the purchaser, whether in contract, tort, or otherwise, for any indirect or consequential loss or damage, loss of use, loss of production, or loss of profits or interest costs, provided that this exclusion shall not apply to any obligation of the supplier to pay penalties and/or damages to the purchaser.

The aggregate liability of the supplier to the purchaser, whether under the contract, in tort or otherwise, shall not exceed the total contract price, provided that this limitation shall not apply to the cost of repairing or replacing defective equipment.

- GOVERNING LANGUAGE

The contract shall be written in English. All correspondence and other documents pertaining to the contract that is exchanged by the parties shall also be written in English.

- APPLICABLE LAW

The contract shall be interpreted in accordance with South African laws, unless otherwise specified in SCC.

- NOTICES

Every written acceptance of a bid shall be posted to the supplier concerned by registered or certified mail and any other notice to him shall be posted by ordinary mail to the address furnished in his bid or to the address notified later by him in writing and such posting shall be deemed to be proper service of such notice.

The time mentioned in the contract documents for performing any act after such aforesaid notice has been given, shall be reckoned from the date of posting of such notice.

- TAXES AND DUTIES

  - A foreign supplier shall be entirely responsible for all taxes, stamp duties, license fees, and other such levies imposed outside the purchaser’s country.

  - A local supplier shall be entirely responsible for all taxes, duties, license fees, etc., incurred until delivery of the contracted goods to the purchaser.

  - No contract shall be concluded with any bidder whose tax matters are not in order. Prior to the award of a bid, GPAA must be in possession of a tax clearance certificate, submitted by the bidder. This certificate must be an original issued by the South African Revenue Services.

# Text boxes

YOU ARE HEREBY INVITED TO BID FOR REQUIREMENTS OF GOVERNMENT PENSIONS ADMINISTRATION AGENCY (GPAA)

THE SUCCESSFUL BIDDER WILL BE REQUIRED TO FILL IN AND SIGN A WRITTEN CONTRACT FORM (SBD7.1 / SBD7.2 / SBD7.3)

THE FOLLOWING PARTICULARS MUST BE FURNISHED (FAILURE TO SO MAY RESULT IN THE BID BEING DISQUALIFIED) ALL STANDARD BIDDING DOCUMENT AS ATTACHED