## Slide 1: MPLS/WAN for GPAA
MPLS/WAN RFB Briefing
Bid GPAA 26/2015 Briefing Session
23 January 2015

## Slide 2
Background
Network upgrade initiative across the enterprise
Network design spanning LAN & WAN
Network redundancy built in
OSPF Routing
Dual Data Centres
Mainframe DR Site combined with Seats DR Sites
DR Site service provider and location may change
GPAA is a CISCO shop
Additional network value add projects on the go

## Slide 3
The Requirement
Services:
Service A – Full MPLS & WAN Solution, including last mile connectivity
Service B – Last mile connectivity to current MPLS service Provider

## Slide 4
The Requirement
Service A – Full MPLS & WAN Solution, including last mile connectivity
  MPLS connectivity to all GPAA sites (List in RFB)
  Last Mile Connectivity to all GPAA sites (List in RFB)
  Layer 2 connectivity between data centres (Including Mainframe DR Site)
  Connectivity to 3rd parties from both data centres (List in RFB)
  Redundant connections to all GPAA offices (both medium and point of presence).
  Metro Ethernet links as well as radio/microwave.
  Multiple VRFs (GPAA and GEPF)
  Architecture
  Security
  SLAs
  QoS
  Reports
  NOC
  Real Time Integration to GPAA Technical Team

## Slide 5
The Requirement
Service B – Last mile connectivity to current MPLS service Provider
  Last Mile Connectivity between current MPLS Provider and all GPAA sites (List in RFB)
  Layer 2 connectivity between data centres (Including Mainframe DR Site)
  Connectivity to 3rd parties from both data centres (List in RFB)
  Redundant connections to all GPAA offices (both medium and point of presence).
  Metro Ethernet links as well as radio/microwave.
  Architecture
  Security
  SLAs
  QoS
  Reports
  NOC
  Real Time Integration to GPAA Technical Team

## Slide 6
The Requirement
Site Connections
  Replication
    Hamilton – Gallo Manor: 200 MBPS
    Hamilton – Mainframe DR: 20 MBPS
  Third Party – From Hamilton and Gallo Manor
    SITA: 10 MPBS
    IS: 10 MBPS
    APN: 10 MBPS
    Internet Breakout: 50 MBPS
  MPLS
    Head Office/Call Centre/Seats DR Site – 40 MBPS
    Regional Offices – 20 MBPS
  VRFs
    GPAA VRF
    GEPF VRF

## Slide 7
The Requirement
Service Provider:
National Footprint
References
SLA Guarantees
Proactive Monitoring
Architecture
Security
QoS
NOC ITIL Compliant
Reporting to GPAA
Handling Changes

## Slide 8
Q & A
Thank You!
MPLS/WAN RFB Briefing